## Slide 1: Fault Tolerant System
CSE-508

## Slide 2: Fault Tolerant System
Course Code: | CSE-508 | Credits: | 03
 |  | CIE Marks: | 90
Exam Hours: | 03 | SEE Marks: | 60
Course Learning Outcome (CLOs): After Completing this course successfully, the student will be able to…
CLOs | Description
CLO1 | Demonstrate an understanding of fault tolerance concepts, including faults, errors, and failures, and explain their impact on system reliability.
CLO2 | Identify and apply various redundancy techniques (hardware, software, time, and information redundancy) to design fault-tolerant systems.
CLO3 | Analyze dependability attributes such as reliability, availability, and safety, and use dependability evaluation techniques like Markov processes.
CLO4 | Design and implement fault-tolerant systems using passive, active, and hybrid redundancy techniques for critical applications.
CLO5 | Evaluate and model system reliability and availability using metrics such as MTTF, MTTR, MTBF, and fault coverage.

## Slide 3: Summary of Course Content
Recommended Books:
Design of Fault-Tolerant Systems by Elena Dubrova, Springer, 2013
Fault-Tolerant Systems by Israel Koren and C. Mani Krishna, Morgan Kaufmann, 2010
Reliable Computer Systems: Design and Evaluation by Daniel P. Siewiorek and Robert S. Swarz, CRC Press, 2011
Sl. | Course Content | HRs | CLOs
1 | Introduction to Fault Tolerance, Faults, and Effects | 2 | CLO1
2 | Dependability Attributes: Reliability, Availability, and Safety | 3 | CLO1, CLO3
3 | Redundancy Techniques: Hardware, Software, Time, and Information Redundancy | 4 | CLO2
4 | Reliability and Availability Evaluation Techniques | 4 | CLO3, CLO5
5 | Markov Processes and State Transition Analysis | 3 | CLO3, CLO5
6 | Passive Hardware Redundancy (TMR, NMR) | 3 | CLO2, CLO4
7 | Active Hardware Redundancy (Standby Sparing, Duplication with Comparison) | 3 | CLO2, CLO4
8 | Hybrid Redundancy: Static and Dynamic Techniques | 3 | CLO2, CLO4
9 | Dependability Modeling and System Evaluation | 4 | CLO3, CLO5
10 | Safety Analysis and Safety-Critical Applications | 3 | CLO3, CLO5
11 | Fault-Tolerant Design Examples and Case Studies | 4 | CLO4, CLO5

## Slide 4: Assessment Pattern
Bloom's Category Marks (out of 90) | Tests (45) | Assignments (15) | Quizzes (15) | Attendance (15)
Remember | 5 | 03 |  | 
Understand | 5 | 04 | 05 | 
Apply | 15 | 05 | 05 | 
Analyze | 10 |  |  | 
Evaluate | 5 | 03 | 05 | 
Create | 5 |  |  | 
Bloom's Category | Test
Remember | 7
Understand | 7
Apply | 20
Analyze | 15
Evaluate | 6
Create | 5
CIE- Continuous Internal Evaluation (90 Marks)
SEE- Semester End Examination (60 Marks)

## Slide 5: Course Plan
Week No | Topics | Teaching Learning Strategy(s) | Assessment Strategy(s) | Alignment to CLO
1 | Introduction to Fault Tolerance, Faults, and Effects | Lecture, Discussion | Quiz | CLO1
2 | Dependability Attributes: Reliability, Availability, Safety | Lecture, Examples, Q&A | Assignment | CLO1, CLO3
3 | Dependability Impairments: Faults, Errors, Failures | Lecture, Case Study | Quiz | CLO1
4 | Redundancy Techniques: Hardware Redundancy | Lecture, Problem-Solving | Assignment | CLO2
5 | Redundancy Techniques: Software, Time, and Information | Lecture, Demonstration | In-Class Exercise | CLO2
6 | Reliability and Availability Evaluation Metrics | Lecture, Numerical Problem Solving | Quiz | CLO3, CLO5
7 | Markov Processes and State Transition Analysis | Lecture, Worked Examples | Assignment | CLO3, CLO5
8 | Passive Hardware Redundancy: TMR, NMR | Lecture, Case Studies | Quiz | CLO2, CLO4
9 | Active Hardware Redundancy: Standby Sparing | Lecture, Group Discussion | Mid-Term Exam | CLO2, CLO4
10 | Active Hardware Redundancy: Duplication with Comparison | Lecture, Demonstration | In-Class Exercise | CLO2, CLO4
11 | Hybrid Redundancy Techniques | Lecture, Examples, Problem-Solving | Assignment | CLO2, CLO4
12 | Dependability Modeling Techniques | Lecture, Group Work | Quiz | CLO3, CLO5
13 | Safety Analysis and Safety-Critical Applications | Lecture, Case Studies | Assignment | CLO3, CLO5
14 | Fault-Tolerant Design Examples and Case Studies | Lecture, Project Discussion | Group Presentation | CLO4, CLO5
15 | Fault Detection and Coverage Techniques | Lecture, Problem Solving | In-Class Problem Solving | CLO2, CLO5
16 | Reliability and Safety Evaluation Using Case Studies | Lecture, Hands-On Activity | Final Project Submission | CLO3, CLO5
17 | Course Review and Final Exam | Recap, Q&A | Final Exam | CLO1, CLO2, CLO3, CLO4, CLO5

## Slide 6: Week 1 Slides 6-14

## Slide 7: Objectives
p. 11 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
understanding fault tolerance
  faults and their effects (errors, failures)
  redundancy techniques
  evaluation of fault-tolerant systems
balance
  concepts, underlying principles
  applications

## Slide 8: Overview
Introduction
  definition of fault tolerance, applications
Fundamentals of dependability
  dependability attributes: reliability, availability, safety
  dependability impairments: faults, errors, failures
  dependability means
Dependability evaluation techniques
  common measures: failure rate, MTTF, MTTR
  reliability block diagrams
  Markov processes
p. 12 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 9: Overview
p. 13 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Redundancy techniques
  space redundancy
    hardware redundancy
    information redundancy
    software redundancy
  time redundancy

## Slide 10: Introduction to Fault Tolerance

## Slide 11: Fault tolerance
p. 15 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
fault-tolerance is the ability of a system to continue performing its function
in spite of faults
broken connection bug in program
hardware software

## Slide 12: Easily testable system
p. 16 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Easily testable system is one whose ability to work correctly can be verified in a simple manner

## Slide 13: Why do we need fault-tolerance?
It is practically impossible to build a perfect system
  suppose a component has the reliability 99.99%
  a system consisting of 100 non-redundant components will have the reliability 99.01%
  a system consisting of 10.000 components will have the reliability 36.79%
It is hard to forsee all the factors
p. 17 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 14: Redundancy
p. 18 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Redundancy is the provision of functional capabilities that would be unnecessary in a fault-free environment
  replicated hardware component
  parity check bit attached to digital data
  a line of program verfiying the correcntess of the resut

## Slide 15: Week 2 Slides 15-23

## Slide 16: History
p. 19 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
early computer systems
  basic components had very low reliability
  fault-tolerant techniques were need to overcome it
    redundant structures with voting
    error-detection and error correction codes

## Slide 17: History
early computer systems
– EDVAC (1949)
  duplicate ALU and compare results of both
  continue processing if agreed, else report error
Bell Relay Computer (1950)
  2 CPU’s
  one unit begin executing the next instruction if the other encounts an error
– IBM650, UNIVAC (1955)
  parity check on data transfers
p. 20 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 18: History
p. 21 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Advent of transistors
  more reliable components
  led to temporary decrease in the emphasis on fault-tolerant computing
  designers thought it is enough to depend on the improved reliability of the transistor to guarantee correct computations

## Slide 19: History
last decades
  more critical applications
    space programs, military applications
    control of nuclear power stations
    banking transactions
  VLSI made the implementation of many redundancy techniques practical and cost effective
  Other than hardware component faults need to be tolerated:
    transient faults (soft errors) caused by environmental factors
    software faults
p. 22 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 20: Applications
p. 23 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
safety-critical applications
  critical to human safety
    aircraft flight control
  environmental disaster must be avoided
    chemical plants, nuclear plants
  requirements
    99.99999% probability to be operational at the end of a 3-hour period

## Slide 21: Applications
mission-critical applications
  it is important to complete the mission
  repair is impossible or prohibitively expensive
    Pioneer 10 was launched 2 March 1970,
passed Pluto 13 June 1983
requirements
    95% probability to be operational at the end of mission (e.g. 10 years)
    may be degraded or reconfigured before (operator interaction possible)
p. 24 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 22: Applications
p. 25 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
bisness-critical applications
  users want to have a high probability of receiving service when it is requested
  transaction processing (banking, stock exchange or other time-shared systems)
    ATM: < 10 hours/year unavailable
    airline reservation: < 1 min/day unavailable

## Slide 23: Applications
p. 26 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
maintenance postponement applications
  avoid unscheduled maintenance
  should continue to function until next planned repair (economical benefits)
  examples:
    remotely controlled systems
    telephone switching systems (in remote areas)

## Slide 24: Week 3 Slides 24-43

## Slide 25: Goals of fault tolerance
p. 27 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
The main goal of fault tolerance is
to increase the dependability of a system

## Slide 26: Dependability
p. 28 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Dependability
is the ability of a system to deliver its intended level of service to its users

## Slide 27: Dependability tree
p. 29 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
dependability
attributes
means
impairments
availability reliability safety
fault tolerance fault prevention fault removal fault forecasting
faults errors failures

## Slide 28: Reliability
R(t) is the probability that a system operates without failure in the interval [0,t], given that it worked at time 0
We need high reliability when:
  even momentary periods of incorrect performance are unacceptable (aircraft, heart pace maker)
  no repair possible (satellite, spacecraft)
p. 30 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 29: High reliability examples
p. 31 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
airplane:
– R(several hours) = 0.999 999 9 = 0.97
spacecraft:
– R(several years) = 0.95

## Slide 30: Reliability versus fault tolerance
p. 32 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Fault tolerance is a technique that can improve reliability, but
  a fault tolerant system does not necessarily have a high reliability
  a system can be designed to tolerate any single error, but the probability of such error to occur can be so high that the reliability is very low

## Slide 31: Reliability versus fault tolerance
p. 33 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
A highly reliable system is not necessarily fault tolerant
  a very simple system can be designed using very good components such that the probability of hardware failing is very low
  but if the hardware fails, the system cannot continue its functions

## Slide 32: How fault tolerance helps
p. 34 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Fault tolerance can improve a system’s reliability by keeping the system operational when hardware or software faults occur
  a computer system with one redundant processor can be designed to continue working correctly even if one of the processors fails
  QUESTION: Will a fault-tolerant system always be more reliable than an individual component?

## Slide 33: Availability
p. 35 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
A(t) is the probability that a system is functioning correctly at the instant of time t
depends on
  how frequently the system becomes non- operational
  how quickly it can be repaired

## Slide 34: Steady-state availability
Often the availability assumes a time- indepentent value after some initial time interval
This value is called steady-state availability Ass
Steady-state availability is often specified in terms of downtime per year
Ass = 90%, downtime = 36.5 days/year Ass = 99%, downtime = 3.65 days/year
p. 36 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 35: Reliability versus availability
p. 37 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
reliability depends on an interval of time
availability is taken at an instant of time
a system can be highly available yet experience frequent periods of being non- operational as long as the length of each period is extremely short

## Slide 36: High availability examples
examples
  transaction processing
    ATM: Ass=0.93 (< 10 hours/year unavailable)
    banking: Ass=0.997 (< 10 s/hour unavailable)
  computing
    supercomputer centres
Ass=0.997 (< 10 days/year unavailable)
  embedded
    telecom: Ass=0.95 (< 5 min./year unavailable)
p. 38 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 37: How fault tolerance helps
p. 39 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Fault tolerance can improve a system’s availability by keeping the system operational when a failure occur
– a spare processor can perform the functions of the system, keeping its available for use, while the primary processor is being repaired

## Slide 38: Safety
p. 40 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Safety is the probability that a system will either perform its function correctly or will discontinue its operation in a safe way
System is safe
  if it functions correctly, or
  if it fails, it remains in a safe state

## Slide 39: High safety examples
p. 41 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
railway signalling
  all semaphores red
nuclear energy
  stop reactor if a problem occur
banking
  don’t give the money if in doubt

## Slide 40: Reliability versus safety
p. 42 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Reliability is the probability that a system will perform its functions correctly
Safety is the probability that a system will either work correctly or will stop in a manner that causes no harm

## Slide 41: How fault tolerance helps
p. 43 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Fault tolerance techniques can improve safety by turning a system off if a failure of a certain sort is detected
– in a nuclear power plant the reaction process should be stopped if some discrepancy is detected

## Slide 42: Summary: attributes of dependability
p. 44 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
reliability:
  continuity of service
availability:
  readiness for usage
safety:
  non-occurrence of catastrophic consequences

## Slide 43: Next lecture
p. 45 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Faults, error and failures
Design philosophies to combat faults
Read chapters 1 and 2 of the text book

## Slide 44: Week 4 Slides 44-53

## Slide 45: Evaluation Techniques

## Slide 46: Two approaches
Qualitative evaluation
  aims to identify, classify and rank the failure modes, or event combinations that would lead to system failures
Quantitative evaluation
  aims to evaluate in terms of probabilities the attributes of dependability (reliability, availability, safety)

## Slide 47: Common dependability measures
failure rate
mean time to failure
mean time to repair
mean time between failures
fault coverage

## Slide 48: Failure rate
failure rate
  expected # of failures per time-unit
  example
    1000 controllers working at t0
    after 10 hours: 950 working
    failure rate for each controller:
0.005 failures / hour
(50 failures / 1000 controllers) / 10 hours

## Slide 49: Failure rate and reliability
Noperating(t)
Noperating(t) Nfailed(t)
R(t) 
Reliability R(t) is the conditional probability that the system will perform correctly throughout [0,t], given that it worked at time 0

## Slide 50: Failure rate
given by
III
II
I
t
bathtub: I infant mortality, II useful life, III wear-out
for useful life period  = constant, the reliability is
typical evolution of (t) for hardware:
(t)
R(t )  et

## Slide 51: Exponential failure law
R(t )  et
If  is constant, R(t) varies exponentially as a function of time
1
0.8
0.6
0.4
0.2
0

## Slide 52: Time varying failure rate
Failure rate is not always constant
– software failure rate decreases as package matures
Weibull distribution:
z(t )  (t ) 1
if =1, then z(t) = constant = 
if >1, then z(t) increases as time increases
if <1, then z(t) decreases as time increases
R(t )  e(t )

## Slide 53: Failure rate calculation
determined for components
  systems: combination of components
   of the system = sum of  of the components
determine  experimentally
  slow
    e.g. 1 failure per 100 000 hours (=11.4 years)
  expensive
    many components required for significance
use standards for 

## Slide 54: Week 5 Slides 54-64

## Slide 55: MTTF
MTTF: mean time to failure
– expected time until the first failure occurs
If we have a system of N identical components and we measure the time ti before each component fails, then MTTF is given by
N
MTTF  1 . ti
N i 1

## Slide 56: MTTF
1


0

dt 
MTTF  e
t
MTTF is defined in terms of reliability as:

MTTF   R(t )dt
0
If R(t) obeys the exponential failure law, then MTTF is the inverse of the failure rate:

## Slide 57: MTTF
1
0.8
0.6
0.4
0.2
0
R(t )  et
R(t)
t
1/ 2/ 3/

## Slide 58: MTTF
MTTF is meaningful only for systems which operate without repair until they experience a failure
Most of mission-critical systems a undergo a complete check-up before the next mission
  all failed redundant components are replaced
  system is returned to fully operational state
When evaluating reliability of such system, mission time rather then MTTF is used

## Slide 59: MTTR
MTTR: mean time to repair
– expected time until repaired
If we have a system of N identical components and ith component requires time ti to repair, then MTTR is given by

N
ti
i 1
1
N
MTTR  .

## Slide 60: MTTR
difficult to calculate
determined experimentally
normally specified in terms of repair rate repair rate  which is the average number of repairs that occur per time period

MTTR  1

## Slide 61: MTTR
Low MTTR requirement implies high operational cost
  if hardware spares are kept on cite and the cite is maintained 24hr a day, MTTR=30min
  if the cite is maintained 8hr 5 days a week,
MTTR = 3 days
  if system is remotely located MTTR = 2 weeks

## Slide 62: MTBF
MTTF
MTTR
MTTF
MTTR
MTBF: mean time between failures
  functional + repair
  MTBF = MTTF + MTTR
small time difference: MTBF  MTTF
conceptual difference
time of 1st failure time of 2nd failure
MTBF
time

## Slide 63: Fault coverage
Fault detection coverage is the conditional probability that, given the existence of a fault, the fault is detected
Difficult to calculate
Usually computed as
C =
number of faults which can be detected total number of faults

## Slide 64: Example
Suppose your circuit has 10 lines and you use single-stuck at fault as a model
Then the total number of faults is 20
Suppose you have 1 undetectable fault
Then the coverage is
19
C = 20

## Slide 65: Week 6 Slides 65-71

## Slide 66: Dependability modelling
up to now:  and R(t) for components
systems are sets of components
system evaluation approaches:
  reliability block diagrams
  Markov processes

## Slide 67: Serial system
system functions
if and only if all components function
reliability block diagram (RBD)

## Slide 68: Serial system
C1
C2
CN
Rseries (t )   Ri (t )
if Ci are independent:
N
series   i
i 1

## Slide 69: Parallel system
system works as long as
one component works
C1
C2
CN

## Slide 70: Parallel system
N
Qparallel(t )   Qi (t )
i 1
if Ci are independent:
N
Rparallel(t )  1  1 Ri (t )
i 1
unreliabity: Q(t) = 1 - R(t)

## Slide 71: Reliability block diagram
RBD
  may be difficult to build
  equations get complex
  difficult to take coverage into account
  difficult to represent repair
  not possible to represent dependency between components

## Slide 72: Week 7 Slides 72-78

## Slide 73: Markov chains
Markov chains
  illustrated by state transition diagrams
idea:
  states
    components working or not
  state transitions
    when components fail or get repaired

## Slide 74: Single-component system, no repair
1
2
Only two states
  one operational (state 1) and one failed (state 2)
  if no repair is allow, there is a single, non-reversible transition between the states (used in availability analysis)
  label  corresponds to the failure rate of the component


## Slide 75: Single-component system with repair
1 2
If repair is allowed (used in availability analysis)
  then a transition between the failed and the operational state is possible
  the label is the repair rate 



## Slide 76: Failed-safe and failed-unsafe
In safety analysis, we need to distinguish between failed-
safe and failed-unsafe states
  let 2 be a failed-safe state and 3 be a failed-unsafe state
  the transition between the 1 and 2 depends on failure rate and the probability that, if a fault occurs, it is detected and handled appropriately (i.e. fault coverage C)
  if C is the probability that a fault is detected, 1-C is the
probability that a fault is not detected
1
2
C
3
(1-C)

## Slide 77: Two-component system
Has four possible states
O O state 1 F O state 2
O F state 3
F F state 4
Components are assumed to be independent and non- repairable
If components are in serial
  state 1 is operational state, states 2,3,4 are failed states
If components are in parallel
  states 1,2,3 are operational states, state 4 is failed state
1
2
1
3
4
2
2
1

## Slide 78: State transition diagram simplification
Suppose two components are in parallel
Suppose 1 = 2 = 
Then, it is not necessary to distinguish between between the states 2 and 3
  both represent a condition where one component is operational and one is failed
  since components are independent events, transition rate from state 1 to 2 is the sum of the two transition rates
 
1 2 3

## Slide 79: Week 8 Slides 79-90

## Slide 80: Markov chain analysis
The aim is to compute Pi(t), the probability that the system is in the state i at time t
Once Pi(t) is known, the reliability, availability or safety of the system can be computed as a sum taken over all operating states
To compute Pi(t), we derive a set of differential equations, called state transition equations, one for each state of the system

## Slide 81: Transition matrix
State transition equations are usually presented in matrix form
Transition matrix M has entries mij, representing the rates of transition between the states i and j
  index i is used for the number of columns
  index j is used for the number of rows
m12 m22
m11 m21
M =

## Slide 82: Single-component system, no repair
entries in each columns must sum up to 0
– entries mii, corresponding to self-transitions, are computed as –(sum of other entries in this column)

1 2
Transition matrix M has the form:
- 0
 0
M =

## Slide 83: Single-component system with repair
Transition matrix M has the form:
1
2


- 
 -
M =

## Slide 84: Single-component system, safety analysis
Transition matrix M has the form:
1
2
C
3
(1-C)
- 0 0
C 0 0
(1-C) 0 0
M =

## Slide 85: Two-component parallel system
Transition matrix M has the form:
1
2
3
 
-2 0 0
2 - 0
0  0
M =

## Slide 86: Important properties of matrix M
Sum of the entries in each column is 0
Positive sign of an ijth entry indicates that the transition originates from the ith state
In reliability analysis, M allows us to distinguish between the operational and failed states
– each failed state i has a zero diagonal element
mii (a failed state cannot leaved)

## Slide 87: State transition equations
Let P(t) be a vector whose ith element is the probability Pi(t), the probability that the system is in the state i at time t
The matrix representation of a system of state transition equations is given by
P(t) = M • P(t)
d dt

## Slide 88: Two-component parallel system
Using transition matrix derived earlier, we get:
This represents the following system of equations
P1(t)
P (t)
2
P3(t)
P1(t) -2 0 0
0
0
P (t) 2 -
2
P3(t) 0 
d dt
=
·
1 1
1 2
P3(t) = P2(t)
d P (t) = -2P (t)
dt
d
dt
d P (t) = 2P (t) - P (t)
dt 2

## Slide 89: Solving state transition equations
By solving these equations, we get
P1(t) = e-2t
P2(t) = 2e-t - 2e-2t
P3(t) = 1- 2e-t + e-2t
Since the Pi(t) are known, we can compute the reliability of the system as a sum of probabilities taken over all operating states
Rparallel(t) = P1(t) + P2(t) = 2e-t - e-2t

## Slide 90: Comparison to RBD result
Since R = e-t, the previous equation can be written as
which agrees with the expression derived using RBD
two results are the same because we assumed that the failure rates of the two components are independent
Rparallel(t) = 2R – R2

## Slide 91: Week 9 Slides 91-102

## Slide 92: Dependant component case
The value of Markov chains become evident when component failures cannot be assumed to be independent
  load-sharing components
  examples: electrical load, mechanical load, information load
If two components share the same load and one fails, the additional load on the second component increases its failure rate

## Slide 93: Parallel system with load sharing
As before, we have four states, but after the 1st component failure, the failure rate of the 2nd component increases
1
2
1
3
4
'2
2
'1

## Slide 94: Parallel system with load sharing
State transition equations are:
2
1
-1-2 0 0 0
1 -'2 0 0
 0 -' 0
0 '2 '1 0
P1(t)
P2(t)
3
P (t)
P4(t)
P1(t)
P2(t)
P (t)
3
P4(t)
d dt
=
·
1 1 2 1
d P (t) = (- - )P (t)
dt
d P3(t) = 2P1(t) -'1P3(t)
dt
d P2(t) = 1P1(t) -'2P2(t)
dt
d P4(t) = '2P2(t)+'1P3(t)
dt

## Slide 95: Effect of the load
If '1= 1 and '2= 2 , the equation of load sharing parallel system reduces to well- known
Rparallel(t) = 2e-t - e-2t

## Slide 96: Availability evaluation
Difference with reliability analysis:
  in reliability analysis components are allowed to be repaired as long as the system has not failed
  in availability analysis components can also be
repaired after the system failure

## Slide 97: Two-component standby system
First component is primary
Second is held in reserve and only brought to operation if the first component fails
We assume that
  fault detection unit which detect failure of the primary component are replace is with standby is perfect
  standby component cannot fail while in the standby mode

## Slide 98: State transition diagram for reliability analysis with repair
1
2

3
1
2
1
-  0
1 -2- 0
0 2 0
M =
state 1: both OK
state 2: primary failed and
replaced by spare
state 3: both failed
Repair replaces a broken component by a working one.

## Slide 99: State transition diagram for availability analysis with repair
-1  0
1 -2- 
0 2 -
M =
1
2
3
 
1 2
States are the same.
Repair replaces a broken component by a working one. Here we assume that there is only one repair team.

## Slide 100: State transition diagram for availability analysis with repair
-1  0
1 -2- 2
0 2 -2
M =
1
2
3
 
1 2
If we assume that there are two independent repair teams, then  on the edge from 3 to 2 gets the coefficient 2 (the rate doubles).

## Slide 101: Availability analysis
None of the diagonal elements of M are 0
By solving the system, we can get Pi(t) are compute the availability as a sum of probabilities taken over all operating states
Usually steady-state availability rather than time
dependent one is of interest
As time approaches infinity, the derivative of the right- hand side of the equation d/dt P(t) = M • P(t) vanishes and we get time-independent relationship
M • P() = 0

## Slide 102: Two-component standby system
A()  1 - (/)2
Using transition matrix derived earlier, we get the following
system of equations
-1P1() + P2() = 0
1P1() – (2+ )P2() + P3() = 0
2P2() – P3() = 0
By solving the equations, we get

## Slide 103: Week 10 Slides 103-110

## Slide 104: Safety evaluation
The state transition equations are:
1
2
C
3
(1-C)
- 0 0
C 0 0
(1-C) 0 0
P1(t)
P (t)
2
P3(t)
P1(t)
P (t)
2
P3(t)
d dt
=
·

## Slide 105: Safety evaluation
At time t=0, the safety is 1. As time approaches infinity, the safety approaches C
By solving these equations, we get
P1(t) = e-t
P2(t) = C(1- e-t)
P3(t) = (1-C) – (1-C)e- t
Since the Pi(t) are known, we can compute the reliability of the system as a sum of probabilities of neing the operational and fail-safe states
R(t) = P1(t) + P2(t) = C + (1-C)e-t

## Slide 106: How to deal with cases of systems with “k out of n choices”
Suppose we want to solve the following task:
What is the probability that more than two engines in a 4-engine airplane will fail during a t-hour flight if the failure rate of a single engine is  per hour?
The probability that more than two engines fail can be expressed as:
P2 failed = ( 4 )P1 works 3 failed + P4 failed
1
= 1 – (P4 work + ( 4 )P3 work 1 failed + ( 4 )P2 work 2 failed )
3 2
Only probabilities of mutually exclusive events can be summed up like this

## Slide 107
= 6
“k out of n choices”
“k out of n choices” can be computed as
For example
k
n!
(n-k)! k!
( n ) =
( 4 ) =
2
4!
(4-2)! 2!

## Slide 108: Example cont.
So, we get
P2 failed = 4 P1 works 3 failed + P4 failed
where
P1 works 3 failed = R (1-R)3 P4 failed = (1-R)4
where R is the reliability of a single engine computed as R = e-t

## Slide 109: Summary
Methods for evaluating the reliability, availability and safety of a system
  RBDs
  Markov chains

## Slide 110: Next lecture
Hardware redundancy
Read chapter 4 of the text book

## Slide 111: Week 11 Slides 111-122

## Slide 112: Hardware redundancy

## Slide 113: Techniques for fault tolerance
p. 2 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Fault masking “hides” faults that occur. Do not require detecting faults, but require containment of faults (the effect of all faults should be local)
Another approach is to first to detect, locate and contain faults, and then to recover from faults using reconfiguration

## Slide 114: Redundancy
hardware redundancy
  2nd CPU, 2nd ALU, ...
software redundancy
  validation test...
information redundancy
  error-detecting and correcting codes, ...
time redundancy
  repeating tasks several times, ...
p. 3 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 115: Example
p. 4 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
FT digital filter
  acceptance test [0 - 255]
    SW: detect overflow
    HW: memory for test
    time: to execute test
  transients: via re-execution
    time to re-execute

## Slide 116: Redundancy (5)
p. 5 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
NOTHING FOR FREE!
costs
  HW: components, area, power, ...
  SW: development costs, ...
  information: extra HW to code / decode
  time: faster CPUs, components
trade-off against increase in dependability

## Slide 117: Types of redundancy
p. 6 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
hardware redundancy
information redundancy
software redundancy
time redundancy

## Slide 118: HW redundancy: overview
p. 7 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
passive redundancy techniques
  fault masking
active redundancy techniques
  detection, localisation, containment, recovery
hybrid redundancy techniques
  static + dynamic
  fault masking + reconfiguration

## Slide 119: Passive HW redundancy
p. 8 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
output
Triple Modular Redundancy (TMR)
voter
M1
input 1
M2
M3
input 2
input 3

## Slide 120: Passive HW redundancy
p. 9 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Triple Modular Redundancy (TMR)
  3 active components
  fault masking by voter
Problem: voter is a single point of failure

## Slide 121: Passive HW redundancy
p. 10 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
V2
M1
in1
M2
M3
in2
in3
V1
V2
M1
M2
V1
V3
in1
in2
in3
out3
out1
out2
V3 M3
restoring organ

## Slide 122: Passive HW redundancy
N-modular redundancy (NMR)
  N active components (N A)
  N odd, for majority voting
  tolerates N/2 module faults
example Apollo
  N=5
  2 faults can be tolerated (masked)
p. 11 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 123: Week 12 Slides 123-130

## Slide 124: HW voting
a
b c
f
0 0 1 0
0 1 1 1
c
f
hardware realisation of 1-bit majority voter f = ab + ac + bc
a
b
n-bit majority voter: n times 1-bit requires 2 gate delays
p. 12 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 125: SW voting
p. 13 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Voting can be performed using software
voter is software implemented by a microprocessor
voting program can be as simple as a sequence of three comparisons, with the outcome of the vote being the value that agrees with at least on on the other two

## Slide 126: HW vs. SW Voting
p. 14 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
HW: fast, but expensive
  32-bit voter: 128 gates and 256 flip-flops
  1 TMR level = 3 voters
SW: slow, but more flexible
  use existing CPUs

## Slide 127: Problem with voting
Major problem with practical application of voting is that the three results may not completely agree
  sensors, used in many control systems, can seldom be manufactured so that their values agree exactly
  analog-to-digital converter can produce quantities that disagree in the least significant bits
p. 15 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 128: Problems with voting
(1) When values that disagree slightly are processed, the disagreement can grow larger
  small difference in inputs can produce large differences in outputs
(2) A single result must ultimately be produced
  potential point where one failure can cause a system failure
p. 16 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 129: How to cure problem 1
time
p. 17 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Mid-value select technique
– choose a value from the three which lies between the other two
value

## Slide 130: How to cure problem 1
p. 18 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Ignore the least-significant bits of data
  disagreement which occurs only in the least- significant bits is acceptable
  disagreement which affects the most-significant bits is not acceptable and must be corrected

## Slide 131: Week 13 Slides 131-144

## Slide 132: Types of HW redundancy
static techniques (passive)
  fault masking
dynamic techniques (active)
  detection, localisation, containment and recovery
hybrid techniques
  static + dynamic
  fault masking + reconfiguration
p. 19 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 133: Active HW redundancy
p. 20 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
dynamic redundancy
  actions required for correct result
    detection, localization, containment, recovery
    no fault masking
  does not attempt to prevent faults from producing errors within the system

## Slide 134: Active HW redundancy
most common in applications that can tolerate temporary erroneous results
– satellite systems - preferable to have temporary failures that high degree of redundancy
types of active redundancy:
  duplication with comparison
  standby sparing
  pair-and-a-spare
  watchdog timer
p. 21 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 135: Duplication with comparison
p. 22 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Two identical modules perform the same computation in parallel and their results are compared
M1
M2
in
out
agree/ disagree
comp

## Slide 136: Duplication with comparison
p. 23 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
The duplication concept can only detect faults, not tolerate them
– there is no way to determine which module is faulty

## Slide 137: Duplication with comparison
Problems:
  if there is a fault on input line, both modules will receive the same erroneous signal and produce the erroneous result
  comparator may not be able to perform an exact comparison
    synchronisation
    no exact matching
  comparator is a single point of failure
p. 24 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 138: Implementation of comparator
p. 25 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
In hardware, a bit-by-bit comparison can be done using two-input exclusive-or gates
In software, a comparison can be implemented a a COMPARE instruction
– commonly found in instruction sets of almost all microprocessors

## Slide 139: Standby sparing
One module is operational and one or more serve as stand-bys, or spares
error detection is used to determine when a module has become faulty
error location is used to determine which module is faulty
faulty module is removed from operation and replaced with a spare
p. 26 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 140: Standby sparing
M1
M2
in
Mn
...
Error detection
Error detection
Error detection
p. 27 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
out
N to 1 switch

## Slide 141: Switch
The switch examines error reports from the error detection circuitry associated with each module
  if the module is error-free, the selection is made using a fixed priority
  any module with errors is eliminated from consideration
  momentary disruption in operation occur while the reconfiguration is performed
p. 28 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 142: Hot standby sparing
p. 29 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
In hot standby sparing spares operate in synchrony with on-line module and are prepared to take over any time
M1
in
out
err
spare
err

## Slide 143: Cold standby sparing
p. 30 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
In cold standby sparing spares are unpowered until needed to replace a faulty module
M1
in
out
err
spare
err

## Slide 144: + and - of cold standby sparing
p. 31 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
(-) time is required to bring the module to operational state
  time to apply power to spare and to initialize it
  not desirable in applications requiring minimal reconfiguration time (control of chemical reactions)
(+) spares do not consume power
  desirable in applications where power consumption is critical (satellite)

## Slide 145: Week 14 Slides 145-163

## Slide 146: Pair-and-a-spare technique
p. 32 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Combines standby sparing and dublication with comparison
like standby sparing, but two instead of one modules are operated in parallel at all times – their results are compared to provide error
detection
– error signal initiates reconfiguration

## Slide 147: Pair-and-a-spare technique
M1
M2
in
Mn
...
Error detection
N to 2 switch
Error detection
Error detection
p. 33 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
out
compare

## Slide 148: Pair-and-a-spare technique
p. 34 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
As long as two selected outputs agree, the spares are not used
If they disagree, the switch uses error reports to locate the faulty module and to select the replacement module

## Slide 149: Watchdog timer
watchdog timer
  must be reset an on a repetitive basic
  if not reset - system is turned off (or reset)
  detection of
    crash
    overload
    infinite loop
  frequency depends on application
    aircraft control system - 100 msec
    banking - 1 sec
p. 35 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 150: HW redundancy: overview
p. 36 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
static techniques (passive)
  fault masking
dynamic techniques (active)
  detection, localisation, containment, recovery
hybrid techniques
  static + dynamic
  fault masking + reconfiguration

## Slide 151: Hybrid HW redundancy
p. 37 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
combines
  static redundancy
    fault masking
  dynamic redundancy
    detection, location, containment and recovery
very expensive but more FT

## Slide 152: Types of hybrid redundancy
p. 38 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Self-purging redundancy
N-modular redundancy with spares
Triple-duplex architecture

## Slide 153: Self-purging redundancy
p. 39 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
All units are actively participate in the system
each module has a capability to remove itself from the system if its faulty
– very attractive feature: maintenance personnel can disable individual modules and replace them without interrupting the system

## Slide 154: Self-purging redundancy
p. 40 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
M1
out
Mn
M2
…
voter
switch
switch
switch

## Slide 155: Basic structure of a switch
p. 41 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Mi
J
KQ
out
initialize
Is output of a module disagrees with the output of the system, its contribution to the voter is forced to be 0 (threshold voter)
voter

## Slide 156: N-modular redundancy with spares
p. 42 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
M1
out
switch
disagreement detector
M2
…
Mn
S1
…
Sm
voter
…
…

## Slide 157: NMR with spares
System remains in the basic NMR configuration until the disagreement vector determines a fault
the output of the voter is compared to the individual outputs of the modules
module which disagrees is labeled as faulty and removed from the NMR core
spare is switched to replace it
p. 43 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 158: NMR with spares
p. 44 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
The reliability is maintained as long as the pool of spares is not exhausted
3-modular redundancy with 1 spare can tolerate 2 faults
to do it in a passive approach, we would need to have 5 modules

## Slide 159: Triple-duplex architecture
p. 45 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Combines duplication with comparison and triple modular redundancy

## Slide 160: Triple-duplex architecture
p. 46 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
out
M1a M1b
comp
M2a M2b
comp
M3a M3b
comp
voter

## Slide 161: Triple-duplex architecture
TMR allows faults to be masked
  performance without interruption
duplication with comparison allows faults to be detected and faulty module removed from voting
  removal of faulty module allows to tolerate future faults
two module faults can be tolerated
p. 47 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 162: Summary
application-dependent choice
  critical-computation - momentary erroneous results are not acceptable
    passive or hybrid
  long-life, high-availability - system should be restored quickly
    active
  very critical applications - highest reliability
    hybrid
p. 48 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 163: Next lecture
p. 49 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Information redundancy
Read chapter 5 of the text book

## Slide 164: Week 15 Slides 164-184

## Slide 165: Information redundancy

## Slide 166: Information redundancy
p. 2 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
add information to date to tolerate faults
  error detecting codes
  error correcting codes
data applications
  communication
  memory

## Slide 167: Code
p. 3 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Code of length n is a set of n-tuples satisfying some well-defined set rules
of
binary code uses only 0 and 1 symbols
binary coded decimal (BCD) code
  uses 4 bits for each decimal digit
0000 0
0001 1
0010 2
…
1001 9

## Slide 168: Code word
Codeword is an element of the code satisfying the rules of the code
Word is an n-tuple not satisfying the rules of the code
Codewords should be a subset of all possible 2n binary tuples to make error detection/correction possible
  BCD: 0110 valid; 1110 invalid
  any binary code: 2013 invalid
The number of codewords in a code C is called the size of C
p. 4 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 169: Encoding/decoding
p. 5 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
code word
encoding
  transform data into code word
data encoding
decoding
  recover data from code word
code word decoding
data

## Slide 170: Encoding/decoding
p. 6 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
2 scenario if errors affect codeword:
  correct codeword  another codeword
  correct codeword  word

## Slide 171: Error detection
p. 7 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
We can define a code so that errors introduced in a codeword force it to lie outside the range of codewords
– basic principle of error detection

## Slide 172: Error detection
p. 8 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
all possible words
code words

## Slide 173: Error correction
p. 9 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
We can define a code so that it is possible to determine the correct code word from the erroneous codeword
– basic principle of error correction

## Slide 174: Error correction
p. 10 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
all possible codewords
code words

## Slide 175: Error detecting/correcting code
Characterized by the number of bits that can be corrected
  double-bit detecting code can detect two single-bit errors
  single-bit correcting code can correct one single-bit error
Hamming distance gives a measure of error detecting/correcting capabilities of a code
p. 11 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 176: Hamming distance
p. 12 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Hamming distance is the number of bit positions in which two n-tuples differ
x 0000
y 0101
 (x,y) = 2

## Slide 177: 3-dimensional space (3-bit words)
010
101
110
011 111
001
0x0yz0 10x0
p. 13 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
y
z
=1

## Slide 178: Error detection
010
101
110
011 111
001
000 100
p. 14 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
If codewords are on distance  2, we can detect single-bit errors

## Slide 179: Error correction
010
101
110
011 111
001
000 100
p. 15 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
If codewords are on distance  3, we can correct single-bit errors

## Slide 180: Code distance
p. 16 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Cd = 2
code distance is the minimum Hamming distance between any two distinct codewords
code detects all single-bit errors code: 00, 11
invalid code words: 01 or 10
Cd = 3
code corrects all single-bit errors code: 000, 111
invalid code words: 001, 010, 100,
101, 011, 110

## Slide 181: Relation b/w code distance and capabilities of the code
p. 17 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
2c + d + 1  Cd
A code can correct up to c bit errors and detect up to d additional bit errors if and only if:

## Slide 182: Separable/non-separable code
separable code
  codeword = data + check bits
  e.g. parity: 11011 = 1101 + 1
non-separable code
  codeword = data mixed with check bits
  e.g. cyclic: 1010001 -> 1101
decoding process is much easier for separable codes (remove check bits)
p. 18 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 183: Information rate
p. 19 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
The ratio k/n, where
  k is the number of data bits
  n is the number of data + check bits
is called the information rate of the code
Example: a code obtained by repeating data three times has the information rate 1/3

## Slide 184: Next: Types of codes
parity codes
linear codes
  Hamming codes
cyclic codes
  CRC codes
  Reed-Solomon codes
unordered codes
  m-of-n codes
  Berger codes
arithmetic codes
  AN-codes
  residue codes
p. 20 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 185: Week 16 Slides 185-192

## Slide 186: Single-bit parity code
Add an extra bit to binary word so that that resulting code word has either even or odd number of 1s
  even parity: even # ‘1’
  odd parity: odd # ‘1’
single bit error detection: Cd = 2
separable code
use: bus, memory, transmission, …
p. 21 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 187: Organization of memory with single- bit parity code
extra HW required (parity generator, checker, extra memory)
p. 22 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
memory
parity
generator
parity
checker
Data in
Data out
Parity Parity
error

## Slide 188: Parity generation and checking
p. 23 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Data bits
1 if odd
d0 d1 d2 d3
error if 1
d0 d1 d2 d3
Parity bit

## Slide 189: Problem with single-bit parity code
p. 24 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Multiple-bit errors (even number of bits) cannot be detected
  some of them are often very common
    failure of the individual memory chip

## Slide 190: Other parity codes
The purpose is to provide additional error capability
  bit-per-word
  bit-per-byte
  bit-per-multiple-chips
  bit-per-chip
  interlaced
  overlapping
p. 25 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 191: Overlapping parity code (Hamming code)
p. 26 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Bit in error | Parity pattern
3 | P2 P1 P0
2 | P2 P1
1 | P2 P0
0 | P1 P0
P2 | P2
P1 | P1
P0 | P0
no error | 
Overlapping parity for 4-bits of data - each data bit is assigned to multiple parity groups
3 2 1 0
P2 P1 P0

## Slide 192: Overlapping parity code (Hamming code)
p. 27 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
k | c | redundancy
2 | 3 | 150%
4 | 3 | 75%
8 | 4 | 50%
16 | 5 | 31%
32 | 6 | 19%
64 | 7 | 11%
k data bits, c parity bits
to have unique parity pattern per error:
2c  k+c+1

## Slide 193: Week 17 Slides 193-209

## Slide 194: Background
p. 28 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
A field Z2 is the set { 0,1} together with two operations of addition and multiplication (modulo 2) satisfying a given set of properties
A vector space Vn over a field Z2 is a subset of Z n, with
2
two operations of addition and multiplication (modulo 2)
satisfying a given set of properties
A subspace is a subset of a vector space which is itself a vector space
A set of vectors {v0,…,vk-1 } is linearly independent if a0v0 + a1v1 + …+ ak-1vk-1 = 0 implies a0 = a1= …= ak-1 = 0

## Slide 195: Cyclic codes
Cyclic codes are special class of linear codes
Used in applications where burst errors can occur
  a group of adjacent bits is affected
  digital communication, storage devices (disks, CDs)
Important classes of cyclic codes:
  Cyclic redundancy check (CRC)
    used in modems and network protocols
  Reed-Solomon code
    used in CD and DVD players
p. 51 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 196: Cyclic code: Definition
p. 52 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
A linear code is called cyclic if any end-around shift of codeword produces another codeword
  if [c0c1c2…cn-2cn-1] is a codeword, then [cn-1c0c1c2…cn-2], is a codeword, too
it is convenient to think of words as polynomials rather than vectors
  for example, a codeword [c0c1…cn-1] is represented as a polynomial
c0·x0+ c1·x1+…+ cn-1 ·xn -1

## Slide 197: Polynomials
p. 53 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Since the code is binary, the coefficients are 0 and 1
For example, d(x) = 1·x0+0·x1+1·x2+1·x3 represents the data (1011)
We always write least significant digit on the left

## Slide 198: Polynomials
The degree of a polynomial equals to its highest exponent
  e.g. the degree of 1+ x1+ x3 is 3
a cyclic code with the generator polynomial of degree (n-k) detects all burst errors affecting (n-k) bits or less
  n is the number of bits in codeword
  k is the number of bits in data word
p. 54 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 199: Encoding/decoding
p. 55 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Encode c(x)=d(x)·g(x)
d(x)
transmit
Decode/Correct d(x)=c(x)/g(x)
d(x)

## Slide 200: Encoding
p. 56 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Multiply data polynomial by generator polynomial:
c(x) = d(x).g(x)
Calculations are performed in Galois Field GF(2):
multiplication modulo 2 = AND operation
addition modulo 2 = XOR operation
in GF(2), subtraction = addition

## Slide 201: Properties of generator polynomial
p. 57 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
g(x) is the generator polynomial for a linear cyclic code of length n if and only if g(x) divides 1+xn without a reminder

## Slide 202: Example of polymomial multiplication (1)
p. 58 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
d(x) = (1011) = x3 + x2 + 1
g(x) = x3 + x + 1
k = 4
c(x) = d(x).g(x)
= (x3 + x2 + 1).(x3 + x + 1)
= x6 + x4 + x3 + x5 + x3 + x2 + x3 + x + 1
= x6 + x5 + x4 + x3 + x2 + x1 + 1
= (1111111)
n = 7

## Slide 203: CRC codes
CRC-16 and CRC-CCITT are widely used in modems and network protocols in the USA and Europe, respectively, and give adequate protection for most applications
  the number of non-zero terms in their polynomials is small (just four)
  LFSR required to implement encoding and decoding is simpler
Applications that need extra protection, e.g.
DD, use CRC-32
p. 79 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 204: Encoding/decoding
The encoding and decoding is done either in software, or in hardware using the usual procedure for separable cyclic codes
To encode:
  shift data polynomial right by deg(g(x)) bit position
  divided it by the generator polynomial
  the coefficients of the remainder form the check bits of the CRC codeword
p. 80 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 205: Encoding/decoding
The number check bits equals to the degree of the generator polynomial
  an CRC detects all burst error of length less or equal than deg(g(x))
CRC also detects many errors which are larger than deg(g(x))
  apart from detecting all burst errors of length 16 or less, CRC-16 and CRC-CCITT are also capable to detect 99.997% of burst errors of length 17 and 99.985% burst errors of length 18
p. 81 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 206: Reed-Solomon codes
Reed-Solomon (RS) codes are a class of separable cyclic codes used to correct errors in a wide range of applications including
  storage devices (tapes, compact disks, DVDs, bar-codes), wireless
  communication (cellular telephones, microwave links), satellite
  communication, digital television, high-speed modems (ADSL, xDSL).
p. 82 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 207: Reed-Solomon codes
The encoding for Reed-Solomon code is done the using the usual procedure
  codeword is computed by shifting the data right n-k positions, dividing it by the generator polynomial and then adding the obtained reminder to the shifted data
A key difference is that groups of m bits rather than individual bits are used as symbols of the code.
  usually m = 8, i.e. a byte.
  the theory behind is a field Zm2 of degree m over {0,1}
p. 83 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 208: Encoding
p. 84 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
An encoder for an RS code takes k data symbols of s bits each and computes a codeword containing n symbols of m bits each
A Reed-Solomon code can correct up to n- k/2 symbols that contain errors

## Slide 209: Summary of cyclic codes
p. 87 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Any end-around shift of a codeword produce another codeword
code is characterized by its generator polynomial g(x), with a degree (n-k), n = bits in codeword, k = bits in data word
detect all single errors and all multiple adjacent error affecting (n-k) bits or less

## Slide 210: Week 18 Slides 209-222

## Slide 211: Unordered codes
Designed to detect unidirectional errors
An error is unidirectional if all affected bits are changed to either 0  1 or 1  0, but not both
Example:
  correct codeword: 010101
  same codeword with unidirectional errors: 110101 000101
111101 000001
111111 000000
p. 88 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 212: Unidirectional error detection
Theorem: A code C detects all unidirectional errors if and only if every pair of codewords in C is unordered
two binary n-tuples x and y are ordered if either xi  yi or xi  yi for all i  {1,2,...,n}
Examples of ordered codewords:
0110 < 0111 < 1111
0110 > 0100 > 0000
p. 89 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 213: Unidirectional error detection
A unidirectional error always changes a word x to a word y which is either smaller or greater than x
A unidirectional error cannot change x to a word which is not ordered with x
Therefore, if any pair of codewords are unordered, a unidirectional error will never transform a codeword to another codeword
p. 90 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab

## Slide 214: Berger code
p. 93 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Append c check bits to k data bits
c = log2(k+1)
separable code
how to create code word:
  count number of 1’s in k data bits
  complement resulting binary number and append it to the data bits

## Slide 215: Example of Berger codeword
p. 94 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
data = (0111010), k = 7
c = log2(7+1) = 3
number of 1’s in (0111010) is 4 = (100)
complement of (100) is (011) resulting codeword is (0111010011)

## Slide 216: Berger code capability
p. 95 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Berger code detects all unidirectional errors
for the error detection capability it provides, the Berger code uses the fewest number of check bits of the available separable unordered codes

## Slide 217: Arithmetic codes
p. 96 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
For checking arithmetic operations
  before the operation, data is encoded
  after the operation, code words are checked
Arithmetic code is the invariant to “*” if:
A(b*c) = A(b) * A(c)
b, c - operands
A(b), A(c), A(b*c) - codes for b, c and b*c

## Slide 218: Examples of arithmetic codes
p. 97 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Two common types of arithmetic codes are
  AN codes
  residue codes

## Slide 219: AN code
If no error occurred, A(b+c) is evenly divisible by A
p. 98 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
AN code is formed by multiplying each data word N by some constant A
AN codes are invariant to addition (and subtraction):
A(b + c) = A(b) + A(c)

## Slide 220: Residue codes
p. 103 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Residue codes are created by computing a residue for data and appending it to the data
The residue is generate by dividing a data by a integer, called modulus.
Decoding is done by simply removing the residue

## Slide 221: Residue codes
p. 104 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Residue codes are invariants with respect to addition, since
where b and c are data words and m is modulus
This allows us to handle residues separately from data during addition process.
Value of the modulus determines the information rate and the error detection capability of the code
(b + c) mod m = b mod m + c mod m

## Slide 222: Next lecture
p. 105 - Design of Fault Tolerant Systems - Elena Dubrova, ESDlab
Time redundancy
Read chapter 6 of the text book