## Slide 1
CE-0732-1201
SURVEYING
Oaisul Mostofa Karim
Lecturer
Dept. of Civil Engineering
University of Global Village (UGV), Barishal

## Slide 2: SURVEYING COURSE CODE: CE-0732-1201 CREDIT: 04 MID EXAMINATION: 2 HOURS CIE MARKS: 120 SEMESTER END EXAMINATION: 3 HOURS SEE MARKS: 80
Course Learning Outcomes (CLOs): After completing this course, students will be able to-
CLO 01 Understand the fundamentals of surveying and linear measurements and develop skills to conduct practical measurements.
CLO 02 Identify the fields of chain surveying and compass traversing and determine offsets, errors and bearings in practical field.
CLO 03 Analyze the area of a specific site for earthwork excavation.
CLO 04 Assess the volume of a specific site to be excavated before starting construction.

## Slide 3
Sl. | Course Contents | Hours | CLOs
01 | Introduction to Surveying, levelling, Objectives, Classifications, Calculation for the Error Due to the Use of Wrong Scale. Introduction to Linear Measurements, Types of Chain, Calculation for the Error Due to the Incorrect Chain and Corrections. | 10 | CLO1, CLO2
02 | Chain Surveying, Errors and Calculations for Chain Surveying, Field Book, Introduction to Compass Traversing, Conversion of Bearing, Calculation of Bearing from Angles, Mathematical Problems related to Compass Traversing. | 10 | CLO1,CLO4
03 | Introduction to GIS and GPS: Definitions, Existing Technology, Application of Google Map, Advantages of GIS, How does a GIS work, GPS definition, Output from it. Introduction to Remote Sensing: Definition, Classifications, Principles and Observation Platforms of it, Application of Remote Sensing, Advantages of it. | 08 | CLO2,CLO3
REFERENCES
1. “Surveying and Levelling” by N N BASAK.
2. “Surveying Vol.1, 2 & 3” By B.C. Punmia.
3. “A Textbook of Surveying” by Aziz and Shahjahan.

## Slide 4
Week | Topic | Teaching Learning Strategy | Assessment Strategy | CLOs | Page No.
01 | Fundamental of Surveying | Lecture, Discussion | Mid, Final | CLO 1 | 
02 | Fundamental of Surveying | Lecture, Discussion | Mid, Final | CLO 1 | 
03-04 | Linear Measurements | Lecture, Presentation | Assignment, Mid, Final | CLO 3 | 
05 | Linear Measurements | Lecture, Presentation | Assignment, Mid, Final | CLO 2 | 
06 | Chain Surveying | Lecture, Presentation | Assignment, Class Test, Mid, Final | CLO 4 | 
07 | Chain Surveying | Lecture, Presentation | Problem solving, Class Test, Final | CLO 4 | 
08-09 | Compass Traversing | Lecture, Discussion | Mid, Final | CLO 4 | 
10 | Calculation of Volume | Lecture, Presentation | Problem solving, Class Test, Final | CLO 3 | 
11-12 | Introduction of GIS and GPS | Lecture, Discussion | Assignment, Mid, Final | CLO 3 | 
13-14 | Introduction to Remote Sensing | Lecture, Presentation | Assignment, Final | CLO 2 | 

## Slide 5
Bloom’s Category Marks (out of 120) | Tests (60) | Assignments (20) | Quizzes (20) | External Participation in Curricular/Co-Curricular Activities (20)
Remember | 10 |  | 10 | Attendance 20
Understand | 10 |  | 10 | 
Apply | 10 |  |  | 
Analyze | 10 |  |  | 
Evaluate | 10 |  |  | 
Create | 10 | 20 |  | 
Bloom’s Category | Tests
Remember | 10
Understand | 15
Apply | 15
Analyze | 15
Evaluate | 15
Create | 10
ASSESSMENT PATTERN
CIE-Continuous Internal Evaluation (120 Marks)
SEE- Semester End Examination (80 Marks)

## Slide 6
Fundamentals of Surveying
(Week 1)

## Slide 7
Fundamentals of Surveying
What is Surveying?
Surveying is the art of determining the relative position of points on, above or below the surface of the earth by means of direct or indirect measurements.
What is Levelling?
This is the branch of surveying which helps in finding the elevations of different points with respect to a reference point.

## Slide 8
Objectives and Uses of Surveying
To determine the relative positions of any objects or points of the earth.
To determine the distance and angle between different objects.
To prepare map or plan.
To develop methods through the knowledge of modern science and technology.
To solve measurement problems in an optimal way.
Fundamentals of Surveying

## Slide 9
Objectives and Uses of Levelling
To determine the elevation of given point with respect to some assumed reference line, which is called datum.
To establish the point at required elevation with respect to the datum.
Fundamentals of Surveying

## Slide 10
Classifications of Surveying
Based on the nature of the field survey:
Land survey (Topographical survey, Cadastral survey, City survey)
Marine survey
Astronomical survey
Fundamentals of Surveying

## Slide 11
Classifications of Surveying
Based on the object of the field survey:
Engineering survey
Military survey
Mine survey
Geological survey etc.
Fundamentals of Surveying

## Slide 12
Classifications of Surveying
Based on the instruments:
Chain survey
Theodolite survey
Traverse survey
Triangulation survey
Tacheometric survey
Plane table survey etc.
Fundamentals of Surveying

## Slide 13
Fundamentals of Surveying
(Week 2)

## Slide 14
Error Due to the Use of Wrong Scale
Fundamentals of Surveying
R.F-Representative Fraction

## Slide 15
Error Due to the Use of Wrong Scale
Fundamentals of Surveying

## Slide 16
Error Due to the Use of Shrunk Scale
Fundamentals of Surveying

## Slide 17
Error Due to the Use of Shrunk Scale
Fundamentals of Surveying

## Slide 18
Linear Measurements
(Week 03-04)

## Slide 19
Chaining
Chaining is a term used to denote measuring distance with the help of chain or tape.
No matter how accurately the angles are measured, survey can be no more precise than that of chaining.
Linear Measurements

## Slide 20
Types of Chain
Metric
Gunter’s / Surveyor’s
Engineer’s
Revenue
Steel band
Linear Measurements

## Slide 21
Types of Chain
Linear Measurements

## Slide 22
Types of Chain
Linear Measurements

## Slide 23
Types of Chain
Linear Measurements

## Slide 24
Types of Chain
Linear Measurements

## Slide 25
Types of Chain
Linear Measurements

## Slide 26
Error Due to Incorrect Chain
Linear Measurements

## Slide 27
Error Due to Incorrect Chain
Linear Measurements

## Slide 28
Error Due to Incorrect Chain
Linear Measurements

## Slide 29
Error Due to Incorrect Chain
Linear Measurements
25-24.88 = 0.12 m = 12 cm

## Slide 30
Linear Measurements
(Week 05)

## Slide 31
Corrections
Corrections for-
Absolute length
Temperature
Sag
Pull
Slope etc.
Linear Measurements

## Slide 32
Corrections
Sag Corrections-
The difference between horizontal distance and measured length along the catenary is termed as Sag.
Linear Measurements

## Slide 33
Corrections
Sag Corrections-
Linear Measurements

## Slide 34
Corrections
Sag Corrections-
Linear Measurements

## Slide 35
Corrections
Pull Corrections-
Linear Measurements

## Slide 36
Corrections
Pull Corrections-
Linear Measurements

## Slide 37
Chain Surveying
(Week 06)

## Slide 38
Chain Surveying
Chain Surveying is a type of surveying in which only linear measurements are made in the field.
Principle: To provide a framework consisting a number of connected triangles, as triangles are the only simple figure in case of chain surveying.

## Slide 39
Chain Surveying
Offsets: Usually offsets are of four types-

## Slide 40
Chain Surveying
Instruments: Generally, the instruments that are used in case of chain surveying are shown here:
Figure: Tape
Figure: Rods

## Slide 41
Chain Surveying
Figure: Wooden Peg
Figure: Arrow
Figure: Plumb Bob

## Slide 42
Chain Surveying
Limiting length of Offsets-

## Slide 43
Chain Surveying
Limiting length of Offsets-

## Slide 44
Chain Surveying

## Slide 45
Chain Surveying

## Slide 46
Chain Surveying
(Week 07)

## Slide 47
Chain Surveying
Chain Surveying can be done in the following steps:
Reconnaissance survey
Fixing stations
Running survey lines

## Slide 48
Chain Surveying
Errors in Chaining: Errors arise in the following ways-
Faulty chain/tape length
Bad ranging
Careless holding & marking
Bad straightening
Sag in chain
Variation in temperature, pull
Personal mistakes

## Slide 49
Chain Surveying
What is “Field Book ?”
The book in which field measurements are entered is termed as field book.
At the beginning of a particular chain survey, what details should be given in a field book?
Date of survey, name of surveyors
Sketch and details of survey lines
Page index of survey lines
Location sketches of survey lines.

## Slide 50
Chain Surveying
Field Book

## Slide 51
Chain Surveying

## Slide 52
Chain Surveying

## Slide 53
Compass Traversing
(Week 08)

## Slide 54
Compass Traversing
Introduction

## Slide 55
Compass Traversing
Introduction

## Slide 56
Compass Traversing
Designation of Bearings

## Slide 57
Compass Traversing
Conversion of Bearing from One System to the Other

## Slide 58
Compass Traversing
Conversion of Bearing from One System to the Other

## Slide 59
Compass Traversing
Fore and Back Bearing
Fore Bearing (FB) - Bearing measured in the direction of progress of the survey.
Back Bearing (BB) - Bearing measured opposite to the direction of survey.

## Slide 60
Compass Traversing
Calculation of Bearing from Angles

## Slide 61
Compass Traversing
Calculation of Bearing from Angles

## Slide 62
Compass Traversing
(Week 09)

## Slide 63
Compass Traversing
Mathematical Problems

## Slide 64
Compass Traversing
Mathematical Problems

## Slide 65
Compass Traversing
Mathematical Problems

## Slide 66
Compass Traversing
Mathematical Problems
Bearing of BA – Bearing of BC

## Slide 67
Calculation of Area

## Slide 68
Calculation of Area

## Slide 69
Calculation of Area

## Slide 70
Calculation of Area

## Slide 71
Calculation of Volume
(Week 10)

## Slide 72
Calculation of Volume
Two Level Section:
Technique to understand - 2 slopes.
Formula for area -
b = the breadth of formation or sub-grade which is usually constant.
n:1 = the side slope (n horizontal to 1 vertical).
1 in m = the transverse slope of the original ground (1 vertical in m horizontal)
h = the height of earthwork (cutting or filling) on the centre line
h1 and h2 = the side heights.
W1 and W2 = the side-widths or half breadths i.e. the horizontal distances from the centre line to the intersections of the side slopes with the original surface.
A = the area of cross-section.
Volume, V=A x L

## Slide 73
Calculation of Volume

## Slide 74
Calculation of Volume
Prismoidal & Trapezoidal Formula:
(P)Volume,
(T) Volume,

## Slide 75
Calculation of Volume

## Slide 76
Introduction to GIS and GPS
(Week 11-12)

## Slide 101
Introduction to Remote Sensing
(Week 13-14)