## Slide 1: CE 4401 Environmental Engineering-II
Prepared By-
Md. Rejoan Chowdhury
Lecturer
Dept. of Civil Engineering
University of Global Village (UGV), Barishal

## Slide 2
Course Learning Outcomes (CLOs): After completing this course, students will be able to-
CLO 01 Understand environmental sanitation system.
CLO 02 Understand the uses of wastewater collection and transportation.
CLO 03 Apply various on-site human waste management systems for construction.
CLO 04 Evaluate solid waste management.
CLO 05 Design pit latrines.
CLO 06 Design septic tank system.
Environmental Engineering-II
COURSE CODE: CE 4401 CREDIT: 04
MID EXAMINATION: 2 HOURS CIE MARKS: 120
SEMESTER END EXAMINATION: 3 HOURS SEE MARKS: 80

## Slide 3
Sl. | Course Contents | Hours | CLOs
1 | Sanitation and health, definition and objectives, disease transmission and sanitation, classification of waste, sanitation systems, important factors for sanitation in Bangladesh. | 4 | CLO 1
2 | OSS, typical sanitation in rural and urban areas, hygiene latrines, pit latrines (simple, VIP, ROEC), operation and maintenance of pit latrine, general design consideration, design of pit latrine, compost latrines. | 8 | CLO 3, CLO 5
3 | Definition of solid waste management (SWM), types of solid waste, functional elements of SWM, generation, on site handling, processing and storage of solid waste, collection of solid waste, sanitary landfill, leachate generation. | 8 | CLO 4
4 | Septic tank system, performance of a septic tank, processes in a septic tank, use of a septic tank, design of a septic tank, septic tank construction, disposal of sludge and scum, soakage pit. | 6 | CLO 6
5 | Conventional sewerage system, important terms, functional elements of a sewerage system, types of collection system, types of sewer, small bore sewerage system. | 6 | CLO 2

## Slide 4
Week | Topic | Teaching Learning Strategy | Assessment Strategy | CLOs | Page No.
1-2 | Introduction to environmental sanitation. | Lecture, Presentation | Mid, Final | CLO 1 | 05-23
3-4 | On site human waste management (1) | Lecture, Presentation | Class Test, Mid, Final | CLO 2 | 24-51
5-6 | On site human waste management (2) | Lecture, Problem solving | Mid, Final | CLO 2 | 52-69
7-8 | Solid waste management (1) | Lecture, Presentation | Assignment, Mid, Final | CLO 2 | 70-87
9-10 | Solid waste management (2) | Lecture, Presentation | Mid, Final | CLO 2 | 88-102
11 | Septic tank system. | Lecture, Discussion | Class Test, Assignment, Final | CLO 3 | 103-114
12-13 | Septic tank design. | Lecture, Problem solving | Class Test, Assignment, Final | CLO 3 | 115-142
14-16 | Wastewater collection and transportation. | Lecture, Presentation | Assignment, Final | CLO 2 | 143-159
References
1. Water supply and sanitation-M. Feroze Ahmed & Md. Mujibur Rahman.

## Slide 5
Bloom’s Category Marks (out of 120) | Tests (60) | Assignments (20) | Quizzes (20) | External Participation in Curricular/Co-Curricular Activities (20)
Remember | 10 |  | 10 | Attendance 20
Understand | 10 |  | 10 | 
Apply | 10 |  |  | 
Analyze | 10 |  |  | 
Evaluate | 10 |  |  | 
Create | 10 | 20 |  | 
Bloom’s Category | Tests
Remember | 10
Understand | 15
Apply | 15
Analyze | 15
Evaluate | 15
Create | 10
ASSESSMENT PATTERN
CIE-Continuous Internal Evaluation (120 Marks)
SEE- Semester End Examination (80 Marks)

## Slide 6
Introduction to Environmental Sanitation
(Week 1-2)

## Slide 7: Background
With the increasing urbanization, industrial development & large human activities, it is natural to increase in the production of wastes.
These waste, if not properly managed/handled/disposed to the environment without treatment/in a state that are harmful to the nature, can have detrimental effects on the environmental quality.
Even though the awareness of the environmental degradation is not yet very prevalent/conscious issue in developing countries like Bangladesh, a major challenge is that of human waste management and disposal.

## Slide 8: Background
Human waste or excreta are the terms used to mean human faeces and urine, excluding other types of domestic waste such as household solid waste of garbage.
These are responsible for spreading of infectious diseases at an uncontrolled rate.
Human wastes are dangerous to health and detrimental to the environment if they are untreated before disposed of into the environment.

## Slide 9: Sanitation and Health
The sanitary disposal of human wastes is arguably of similar importance to safe water supply because it essentially removes the risk of contamination of water by pathogens contained in human faeces.
In addition to public health improvement, investment in sanitation have other benefits in the form of environmental conservation, employment generation, increase in production and a nutrition's for food productivity and water for agriculture.
Appropriate sanitation provides several important facts such as privacy, convenience and health.
It is important to understand that that the improvement of health is not possible without sanitary disposal of human excreta.

## Slide 10: Sanitation and Health
However, neither sanitation nor water supply alone is good enough for health improvement.
It is well established that health education or hygiene promotion must accompany sufficient quantity of safe water and sanitary disposal of excreta to ensure the control of water & sanitary related diseases.

## Slide 11
Interrelationship among water, sanitation,
hygiene education and health

## Slide 12: Definition and Objectives of Sanitation
Sanitation may be defined as the science and practice of effecting healthful and hygienic conditions, and involves the study and use of hygienic measures such as
safe, reliable water supply;
proper drainage of wastewater;
proper disposal of all human wastes;
prompt removal of all refuse.
The prime objectives of providing sanitation facilities:
to have improve public health.
to minimize environmental pollution

## Slide 13: Disease Transmission and Sanitation
Sanitation can greatly prevent the spread of infectious diseases:
1. Ingestion of food or drinking waste.
2. Ingestion of meat infected with tape worms.
3. Contact with contaminated water.
4. Contact with contaminated soil.
5. Insect vectors.

## Slide 14: Disease Transmission and Sanitation

## Slide 15: Classification of wastes
Human waste or human excreta
Municipal sewerage wastewater
Domestic sewerage
Sullage
Industrial waste
Storm water
Solid waste

## Slide 16: Sanitation Systems
A sanitation system involves all arrangement necessary to store, collection, process and deliver human wastes or other forms of wastes back to nature in a safe manner.
Sanitation systems with respect to human waste management has the following function to perform:
Excretion and storage
Collection and transportation
Process/Treatment
Disposal/Recycle.

## Slide 17: Sanitation Systems
On-site : When the waste are collected, treated and disposed of at the point of generation, it is called an on-site system, e.g. Pit latrine and Septic tank system.
On-site sanitation systems are not feasible because of high population density, high water consumption, low infiltration rate of soil or high ground water table, wastes have to be collected and transported off- site for treatment and/or disposal

## Slide 18: Sanitation Systems
Off-site: When these waste is collected and transported to somewhere else for treatment and disposed, the system is called off-site, e.g. bucket latrine systems and conventional sewerage systems.
The basic elements of off-site sanitation system therefore include collection, transportation, treatment, disposal and/or reuse.
The waste is collected either through house sewer or manually using buckets or vaults, transported either by cart, truck or sewer system to a suitable distant place where it is treated prior to disposal or reuse.

## Slide 19: Sanitation Systems
Dry system: In dry system, no water is used for the dilution of the water. They are usually applied in unsewered areas with no piped water supply, e.g., Pit latrine systems (on-site) and Bucket latrine systems (off site).
Wet system: In the wet system the waste is diluted with flushes of water. Wet systems are suitable where piped water supply systems are available, e.g., Septic tank system (on site) and conventional sewerage system (off-site).

## Slide 20
Sanitation Systems Based on Population Density and Water Supply

## Slide 21: Important factors for sanitation in Bangladesh
Housing density: Simple pit latrines are suitable for use in rural areas and low density urban areas up to about 300 people per hectare. Average household size, housing design, plot layout and area have a large influence. At higher densities alternating double pit latrines may be feasible, but other options, such as small bore sewers, community latrine cum biogas plant, etc. may be more appropriate solution.
Water supply service level: In areas water use is low (less than 30l/c/d) and where water has to be hand- carried from public stand-post, tubewell or community wells are feasible. Pit latrines of one type or another are technically feasible sanitation options.

## Slide 22: Important factors for sanitation in Bangladesh
Difficulties associated with pit latrines: Digging pits in loose and unconsolidated soils (e.g., sand or fine-grained alluvium) is difficult and lining must not prevent the seepage of faecal liquids out of the pit into the surrounding soil.
Operation and maintenance: Squatting slabs easily become fouled and pour-flush bowls may block up. The water seal, the essential part of the pour-flush pit latrine, often breaks down. Sometimes other garbage thrown into pan blocks the latrine.

## Slide 23: Important factors for sanitation in Bangladesh
Soil permeability: Soils with permeability below 2.5 mm per hour (expansive clay) are unsuitable for pit latrines, as the liquid fraction of the excreta is unable to infiltrate into soil,thereby leading to overflow of the pits.
Groundwater pollution: The deposition of excreta in pits may pollute water sources, particularly wells, tube-wells, pond, etc., located nearby. The danger of pollution increases if the pit is dug down to the water table or to fissured or weathered rock.
Users are required to locate pits at least 10 m away from tubewells or other water sources to avoid potential pollutions.

## Slide 24: Reference Book
WATER SUPPLY & SANITATION ENGINEERING
by M. Feroze Ahmed, Ph.D &
Md. Mujibur Rahman, Ph.D
[ITN-Bangladesh]

## Slide 25
On Site Human Waste Management (1)
(Week 3-4)

## Slide 26
OSS: User Interface; Containment; OSS Facility;
FSM Services
User interface
Containment (septic tank; pit)
Latrine/OSS Facilities: usually refers to [User interface + Containment]
FSM Services:
Emptying, transport, treatment and disposal
Onsite Sanitation system (OSS):
[User interface + Containment + FSM]

## Slide 27
User Interface
Sanitation
Facility
Containment
FSM Services
Complete Onsite Sanitation System (OSS)
OSS: User Interface; Containment and
Sanitation System

## Slide 28: Preferred Sanitation Facility: Hygienic Latrines
A wide range of on-site sanitation technologies exist and can be selected for use in different hydrological, socio-economic, and cultural conditions.
How do you define a good sanitation facility?
Commonly referred to as a “hygienic latrine”
What is a “hygienic latrine”?

## Slide 29: Hanging Latrine in an Urban Slum

## Slide 30: Typical Sanitation Facilities in Rural Areas

## Slide 31: Typical Sanitation Facilities in Rural Areas

## Slide 32: Typical Sanitation Facilities in Rural/ Low-Middle Income Urban Areas

## Slide 33: Typical toilets in urban areas

## Slide 34: No Containment
Good User Interface

## Slide 35: What is a Hygienic Latrine?
A “hygienic latrine” is defined as a sanitation facility, which effectively breaks the cycle of disease transmission.
A hygienic latrine would include all of the following:
Confinement of waste (excreta),
A barrier (e.g. water seal) in the passage between the squat hole and the pit to effectively block pathways for flies and other insect vectors, thereby breaking the cycle of disease transmission, and
Venting out of foul gases generated in the pit through a properly positioned vent pipe to keep latrine odor free and encourage its continual use.

## Slide 36: Hygienic or Sanitary Latrine
The most fundamental health objectives of sanitation must be achieved through proper design, installation, and use of a sanitary or hygienic latrine.
There is no universal design of a sanitary/ hygienic latrine that could be used for all socio-economic and hydro-geologic conditions.
Therefore, a wide range of sanitary/ hygienic latrine technologies should be available to suit different conditions.

## Slide 37
Sanitation Technologies Commonly used in
Rural and Low-income Areas
Major technological options are:
Pit Latrines (for areas with “limited” water supply)
Pour Flush Latrines
(often both types are referred to as “pit latrines”)

## Slide 38: Pit Latrines:
Only for areas with “limited” water supply
What is “limited water supply”?
Common in water-scarce areas, including many countries in Africa

## Slide 39: Pit Latrines:
A pit is simply a hole in the ground that receives human waste. Urine and other liquids soak into the ground and solid materials are retained and decomposed in the pit.
A pit latrine is designed such that it could operate without the requirement of “flushing”.
Since no flushing water is used, these are sometimes referred to as “dry toilets”.

## Slide 40: Pit Latrines
The major types of pit latrines:
Simple or “Home-made” Pit Latrines
Ventilated Improved Pit (VIP) Latrine
Reed Odourless Earth Closet (ROEC)

## Slide 41: (1) Simple or “Home-Made” Pit Latrine
Compacted earth
Ground level
Infiltration of liquid
Earth
Super structure
Cover
Squatting Slab
Pit
Accumulated solids
A manually dug/ bored hole
A seat or squatting slab
A superstructure
Preferred option when
water availability is limited
Note: When “flushing water” is available, “pour- flush” latrine is preferred option.

## Slide 42: (1) Simple or “Home-Made” Pit Latrine
The simplest “home-made” latrine is built by digging a small hole and placing a platform (concrete, bamboo) on it.
One can use a concrete squatting slab and a ring for an improved version.
This option, though not fully sanitary, is sometimes promoted to discourage open defecation.

## Slide 43: (1) Types of Simple or “Home-Made” Pit Latrine
Accumulated solids
Accumulated solids
Water Sealed
Trap
Pit
Pit
Pit
Earth
Earth
Direct Pit
Partially Offset Pit
Offset Pit
Off-set pit would required flushing (feasible with pour-flush system)

## Slide 44: (1) Types of Simple or “Home-Made” Pit Latrine
Direct pit latrines: Some risk in the stability of the superstructure, particularly when the soil underneath is loose and when the pit is submerged during the wet season.
Partially offset pit latrines: Relatively stable.

## Slide 45
(1) Simple Pit Latrine:
Advantages and Disadvantages
Advantages:
Least costly
Easily constructed
Offers better solution than open defecation Disadvantages:
Not hygienic; spreading of diseases by flies (a properly designed cover can partially solve this problem)
Odor nuisance (a properly designed vent pipe can solve this problem)
Aesthetically less attractive
Improper pit construction may lead to pit collapse

## Slide 46: (2) Ventilated Improved Pit (VIP) Latrines
Slab with squat
hole
Solids
accumulation
Vent pipe
Pit lining
Fly screen
min. 300 mm
Superstructure
Liquid infiltration
Pit partially offset
Provision of “vent pipe”
[Considered to be a good sanitation option in certain parts of the world, where water availability is limited]

## Slide 47: (2) Alternating Twin-Pit VIP Latrines
Two separate pits, with the superstructure located centrally over the off-set pits
The slab covering the pits has two squat holes, one over each pit
Can use permanent superstructure

## Slide 48: (3) VIP Latrines
General:
Overcome disadvantages of simple pit latrines (e.g., fly and mosquito problems, odor)
However, not “sanitary/ hygienic” Single Pit VIP:
Suitable, specially where mechanical pit-emptying is possible
Twin Pit VIP:
One pit used at a time. When one pit is full (1-3 years), it is closed, and the second pit is put into service
When the second pit becomes full, the contents of the first are removed and put back into service. The cycle continues.

## Slide 49: Advantages:
(2) VIP Latrines: Advantages and Disadvantages
Controls odor and insects to a large extent
Relatively low-cost, easily constructed
Twin pits offers long-term solution
Disadvantages:
Absence of “seal” between squat hole and pit prevents is from becoming a “sanitary/ hygienic latrine”.

## Slide 50: (3) Reed Odorless Earth Closet (ROEC)
Chute
Liquid Infiltration
Accumulated solids
Concrete cover
Vent pipe
Air
Seat
Air
Fly screen
A variation of VIP latrine
Pit fully “off-set” from superstructure, and connected to squatting slab with a “curved chute”
Connected with vent pipe to control odor and insect nuisance
Why reduced insect nuisance in VIP and
ROEC?

## Slide 51: Odor and Fly Control: VIP/ ROEC Latrines
Odor Control:
Wind blowing across the top of vent pipe creates circulation of air
Unpleasant odor from pit are thus sucked up through the vent pipe, leaving the toilet odor-free.
Fly Control:
Flies enter the pit via squat hole (to lay egg)
On their way out, they instinctively fly towards “light”
If the latrine door is closed and the latrine is dark inside, only light they can see is at the top of vent pipe.
Since the vent pipe is provided with fly-screen, flies are unable to escape and eventually die.

## Slide 52: (3) ROEC: Advantages and Disadvantages
Advantages:
Controls odor and insects to a large extent (like VIP)
ROEC pit can be made larger, as the superstructure is fully off-set (thus, longer life)
Pit can be easily emptied without disturbing superstructure; hence can be a permanent facility
Structurally more stable
Aesthetically more acceptable
Disadvantages:
Like VIP latrines, not fully “sanitary/ hygienic”
In the absence of flushing, the “chute” easily becomes fouled and needs regular cleaning

## Slide 53
On Site Human Waste Management (2)
(Week 5-6)

## Slide 54: Pit Latrines
Are the different forms of “pit latrines” “hygienic”?
Compare with the 3 criteria of a “hygienic latrine”

## Slide 55: Operation and Maintenance of Pit Latrines
Important operational aspects include the followings:
Regular cleaning of the squatting slab with some water and a little disinfectant if available. In case of ROEC, the chute has to be cleaned regularly.
For “simple pit latrine”, a tight fitting lid may be placed on the squatting hole after every use to ensure insect and odor control.
In case of ROEC/ VIP latrines, the squat hole should never be covered to ensure continuous airflow; rather the door of latrine should be kept closed for keeping inside dark.
Some water should always be available in or near the latrine for cleansing.
Ash or sawdust can be sprinkled occasionally in the pit to reduce smell and insect breeding.
Non-biodegradable material like stones, glass, plastics, rags etc. should not be thrown into the pit as they reduce the effective volume of pit.

## Slide 56
Fecal Sludge Management (FSM) service: Often absent
Absence of FSM -A Common and Major Problem in all Pit Latrines
In the absence of FSM service, when a pit becomes full (up to the design level), there are two options:
  Construct a new pit (and move the superstructure); fill the old pit with soil. This is often problematic due to lack of space, and also due to additional cost involvement.
  Desludge the pit, and dispose the emptied fecal sludge safely (e.g., buried). This is even more problematic. Mechanical desludging facility are often not available; manual desludging is hazardous. Emptied sludge is often disposed in water bodies.

## Slide 57: General Design Consideration of “Pits”
Pit should be as large as possible, but should not exceed 1.5 m. Otherwise, the cover slab become too expensive.
Pits in unstable soil should be lined (concrete rings most common; bricks with cement mortar joints).
Soil with low permeability (below 2.5 mm/hour) are unsuitable for pit latrines.
Prevention of groundwater pollution: A horizontal distance of 10 m between pit and source of drinking water; and a vertical distance of 2 m between pit bottom and highest groundwater level (thumb-rule)

## Slide 58: Prevention of Groundwater Pollution: Thumb Rule
2.0 m
10.0 m

## Slide 59: Typical “Pit” Construction
Typical “pit” in loose/ unconsolidated soil
Typical dimension of each ring: Diameter:  3 feet/ 1 m/ 4 ft
Height: 1 feet/ 0.3 m
Typical “pit” in relatively stale soil
Depth of Pit:
5 to 6 ring (i.e., 1.5 to 1.8 m) are most common
(Not common)
Wall thickness: 1.25Dr.tMouh1am.m5a0d AsihnrfcAlhi- Janu(amry 2a02n0 ually dug pit)

## Slide 60
Maximum depth of manually
excavated pit
In most circumstances, the maximum depth of manually dug pit is about 1.8 m (equivalent to 6 rings).
Unless otherwise specified, consider a maximum depth of 1.8 m for manual excavation.
However, note that in many areas of the country, it is possible to construct deeper pits (especially with mechanical means).

## Slide 61: Design of “Pit” for “Pit Latrines”
Design Considerations:
Sufficient volume for storage and digestion of waste
Infiltration of water not specifically considered (because minimum water use/ no flushing)

## Slide 62: Design of “Pit” for “Pit Latrines”
Effective Volume of Pit, Veff = C x P x N
V = Effective volume of pit in m3
C = Solid accumulation rate (m3/person/yr) P = Number of users
N = Design life (years)
Design Solids Accumulation Rate (C):
Wet pit: 0.04 m3/person/yr (Pour-flush latrines)
Dry pit: 0.06 m3/person/yr (Pit latrines)
Effective Height of Pit, Heff = Veff / A
A = x-sectional area of pit
Total Height of Pit: H = Heff + 0.5 m
0.5 m
Effective pit volume

## Slide 63: Design of “Vent Pipe/System”
Material:
PVC; uPVC; GI; Brick
Choice depends on: durability, availability, cost, ease of construction
Height/ Position (pipe top):
500 mm higher than roof (flat roof)
500 mm above highest point in roof (sloping roof)
Internal diameter:
A ventilation rate of 20 m3/hr (depends on roughness of pipe, length, head loss through fly screen, wind direction, etc.)
Recommended size:
PVC: 150 mm diameter
Brick: 230 mm square
Others: 230 mm diameter

## Slide 64: Design of “Vent Pipe/System” (contd.)
Specification for Fly-screen:
Purpose: To prevent passage of mosquito, flies
Size: Aperture  1.2 mm x 1.5 mm
Material: Corrosion resistant, able to withstand intense rainfall, high temperature, sunlight, preferably stainless steel

## Slide 65: Design Problems
(1) Local authority in a village is offering pre-cast concrete rings of
1.0 m diameter and 0.3 m depth, and concrete slab to cover it at a subsidized price. Design a pit latrine for a family of 7, with maximum possible design life. The soil is unconsolidated/ loose, and the groundwater table is 5.0 m below ground surface.
Water availability in the area is limited. What kind of latrine would you suggest? (a) Simple (direct/ partially offset/ fully offset); (b) VIP; (c) ROEC.
Draw a neat sketch showing all elements of the designed latrine.

## Slide 66: Design Problems
(2) Repeat the same problem if groundwater table is 3.7 m below ground surface.
What would be design life of the pit, if 1.5 m dia concrete rings are used, instead of 1.0 m dia rings.
(increase in diameter of pit significantly increases design life)

## Slide 67: Pit diameter – Pit capacity
Dia = 1 m
Dia = 1.25 m
Dia = 1.50 m
Capacity = V
Capacity = 1.6 V
Capacity = 2.25 V
Increase in diameter of pit significantly increases design life

## Slide 68: Compost Latrines
Principle: aerobic decomposition of feces generates sufficient heat to destroy pathogens and forms good soil conditioner/fertilizer
Necessary conditions for compost process include:
  Appropriate C/N ratio,
  Low moisture content ,
  Access to air
Two types:
Continuous compost latrine
Batch compost latrine

## Slide 69: Continuous Compost Latrine (“Maltrum” type)
Good operation requires about 8 times as much vegetable waste as feces be added to give a suitable C/N ratio.
Has not been very successful in developing countries including Asia.

## Slide 70: Batch (Vault) Compost Latrine
Has two watertight
chambers or vaults
Fillers are added to provide carbon to achieve desired C/N ratio.
Not suitable for areas where water is used for cleaning.
Double Vault Compost Latrine

## Slide 71
Solid Waste Management (1)
(Week 7-8)

## Slide 89
Solid Waste Management (2)
(Week 9-10)

## Slide 104
Septic Tank System
(Week 11)

## Slide 105: Septic Tank System
“Septic Tank System” consists of:
A “Septic Tank” + System/ arrangement for
disposal of septic tank effluent (e.g., soakage pit)

## Slide 106: Septic Tank System
(Septic Tank  Soakage Pit)
Major Option in All Urban Areas (including some Slums)
Sludge
Scum
Sludge

## Slide 107: Septic Tank

## Slide 108: Septic Tank
A septic tank is a buried, water tight receptacle, designed and constructed to receive wastewater from a home.
Its purpose are to separate solids and scum from liquid, to provide limited digestion of organic matter, to store solids, and to allow the clarified liquid to discharge for further treatment and disposal

## Slide 109: Performance of a Septic Tank
Under normal design conditions:
BOD removal
SS removal
: 25 – 50%
: up to 70%
“Detention time” is the most important factor governing performance.
Other factors affecting performance include:
position of inlet and outlet devices in tank
- ambient temperature
nature of influent wastewater
organic content

## Slide 110: Processes in a Septic Tank
4 major processes:
Separation of suspended solids
Digestion/ decomposition of sludge and scum
Stabilization of liquid (i.e., decomposition of organic matter)
Growth of microorganisms

## Slide 111: Processes in a Septic Tank
Separation of Suspended Solids and Scum: Results in the formation of:
  a “sludge layer” at the bottom
  a floating layer of scum at the top
  a relatively clear layer of liquid in the middle

## Slide 112: Processes in a Septic Tank
Digestion/ decomposition of Sludge and Scum: Anaerobic bacteria decomposes organic matter in sludge and scum, and produces volatile acids, methane (CH4).
The formation of gases in the sludge layer causes irregular floatation of sludge flocs that settle after the release of gas at the surface.
Stabilization of Liquid:
Organic materials in the liquid are also stabilized by anaerobic decomposition

## Slide 113: Processes in a Septic Tank
(4) Growth of Microorganisms:
A large variety of microorganisms grow, reproduce and die during biodegradation processes in the tank. Most of them are separated out (by settling) with solids.
However, a large number of microorganisms (bacteria, virus, protozoa, helminthes) survive the processes in the tank and remain in the effluent, the sludge and scum

## Slide 114: Use of Septic Tank System
Predominant system in areas with “piped water supply”.
Also used with “pour flush” toilets, particularly in communal toilets in urban slums and low-income communities (LICs)
In many cases, only septic tank is used without soakage pit [primarily due to lack of awareness, lack of space, due to poor infiltration capacity of soil, and to save money]

## Slide 115: Pour-flush toilet with Septic Tank in Kallyanpur Pora Bosti

## Slide 116
Septic Tank Design
(Week 12-13)

## Slide 117: Design of Septic Tank
Based on Brazilian Septic Tank Code
The tank is considered to be made up of 4 zones, each
serving a different function
  Scum storage zone
  Sedimentation zone
  Sludge digestion zone
  Digested sludge storage zone

## Slide 118: Design of Septic Tank (contd.)
(1) Volume required for Sedimentation:
Time allowed for sedimentation of settable solids is given by:
th = 1.5 – 0.3 log10(Pq)
where, th = minimum hydraulic detention time (days)
P = population served by septic tank
q = wastewater flow (lpcd)
 Tank volume (m3) required for sedimentation,
Vh = 10-3 P.q.th
[Note: A minimum detention
time of 1 day is often used.
The value of th should not be less than 0.2 days]
Sedimentation zone (Vh)

## Slide 119: Design of Septic Tank (contd.)
(2) Volume required for Sludge Digestion:
Tank volume (m3) required for digestion of sludge is given by,
Vd = 0.5 x 10-3 P.td
where, td = time (days) needed for anaerobic digestion of sludge P = population served by septic tank
td varies with temperature (T, °C), and is given by (Mara, 1996), td = 30 (1.035)35-T
Sludge digestion zone (Vd)

## Slide 120: Design of Septic Tank (contd.)
(3) Volume required for Sludge Storage:
Tank volume (m3) required for storage of sludge is given by,
Vsl = C x P x N
C = rate of accumulation of digested sludge
= 0.06 m3/person/yr, for N < 5
= 0.04 m3/person/yr, for N > 5
P = population served by septic tank
N = desludging interval (years)
Sludge storage zone (Vsl)

## Slide 121: Design of Septic Tank (contd.)
(4) Volume required for Scum Storage: Scum accumulation rate
= 30 – 40% of sludge accumulation rate
Thus, Vsc = 0.40 Vsl
where, Vsc = Scum storage volume, and Vsl = Sludge storage volume
Scum Storage (Vsc)

## Slide 122: Design of Septic Tank (contd.)
Total Effective Volume of Septic Tank,
V = Vsc + Vh + Vd + Vsl
Based on experience, effective depth of a septic tank is usually set between 1.0 to 1.5 m (deeper tanks may be designed, if there is space constraint).
Higher x-sectional area is advantageous; hence, for the first trial, select an effective depth of about 1.0 m, and determine the x-sectional area “A” (round off to nearest reasonable value).
Then proceed with determination of effective depth of each zone (i.e., Vzone/A). Special consideration is required for sedimentation zone (as explained below).
A free board of about 250 mm (0.25 m) is usually kept

## Slide 123: Design of Septic Tank (contd.)
Depth of sedimentation zone and “depth of clear space” (see “Fig.) are estimated as follows:
Depth of sedimentation zone, h = Vh / A
Minimum clear space depth = (a + b) = 0.075 + dsc
a = submerged scum clear depth (distance between underside of the scum layer and the bottom of outlet “tee”)
= at least 75 mm (0.075 m) b = dsc = sludge clear depth
(distance between the top of sludge layer and
bottom of outlet “tee” dsc = 0.82 – 0.26A (minimum 0.3m)
Compare “h” with “(a+b)”, and
use the greater depth in design.

## Slide 124: Design of Septic Tank (contd.)
Depth of sedimentation zone and “depth of clear space” (see “Fig.) are estimated as follows:
Depth of sedimentation zone, h = Vh / A
Minimum clear space depth = (a + b) = 0.075 + dsc
a = submerged scum clear depth (distance between underside of the scum layer and the bottom of outlet “tee”)
= at least 75 mm (0.075 m) b = dsc = sludge clear depth
(distance between the top of sludge layer and
bottom of outlet “tee” dsc = 0.82 – 0.26A (minimum 0.3m)
Compare “h” with “(a+b)”, and
use the greater depth in design.

## Slide 125: Design of Septic Tank: Other Considerations
Shape and Dimension:
  Tanks with greater surface area and reasonable depth (usually 1.0 to 1.5 m) are preferred, since higher surface area increases surge storage capacity
  Rectangular perform better than square tanks; cylindrical tanks have also been found satisfactory
  Common shape and dimension of single- compartment septic tanks:
Rectangular with length three times the width

## Slide 126: Design of Septic Tank: Other Considerations
Compartments:
  Properly designed single compartment tanks usually provide acceptable performance
  But a two-compartment tank is reported to perform better than a single-compartment tank
of same capacity in removing BOD, SS and organic colloids.
  Common form of septic tanks: Two compartments;
First compartment (inlet side) being 2/3 of the
total length, while second compartment being 1/3 of the total length

## Slide 127: Design of Septic Tank: Inlet Device
Wastewater should enter septic tank without causing much disturbance to the sedimentation process; and the outflow of a septic tank should carry minimal settleable solids, and no scum.
Inlet Device:
  A “sanitary tee” (see figure); or
  An “elbow”; or
  A specially designed inlet device
Vertical leg of inlet tee should extend below liquid surface, to minimize turbulence

## Slide 128: Design of Septic Tank: Inlet Device
Inlet Pipe:  100 mm diameter, and gradient not steeper than 1.5% for at least 10 m (for protection against surge flow)
Inlet T-junction: diameter should not be less than the diameter of the inlet pipe. The top limb should rise  50 mm above scum level; the bottom limb should extend up to 20% of liquid depth.
20% of liquid
depth
Scum
50 mm

## Slide 129: Design of Septic Tank: Outlet Devices
Ability of outlet device to retain sludge and scum is a major factor in the overall performance of a septic tank
Outlet Device:
A “sanitary tee” (see figure)
Bottom of vertical leg should extend up to 30-40% of liquid depth (minimum 75mm)
Top of vertical leg must should rise
 50 mm above scum level
(so that relatively clear liquid from
sedimentation zone could be discharged through the outlet pipe)
Scum
50 mm

## Slide 130: Design of Septic Tank: Partition Wall
The bottom of partition wall (for two-chamber septic tank) should be at least 75 mm below the bottom of scum level
The partition wall should have a clear opening of about 150 mm
If brick partition wall is constructed, openings of appropriate size are left for passage of liquid
75 mm
150 mm

## Slide 131: Venting of Foul Gas
Septic tanks should be provided with a vent pipe for release of gases generated within the septic tank.
Design considerations are similar to those used for venting system in pit/pour-flush latrines; commonly 50 mm diameter pipes are used for venting.

## Slide 132: Improving Septic Tank Effluent Quality [See “Class Note 5A: ABR”]
Quality of septic tank effluent can be significantly improved by incorporating and “upflow filter bed” near the outlet of septic tank (see fig).
BOD reduction takes place through the growth of anaerobic bacteria on the surface of filter aggregate/ material.
BOD reduction of 70% has been reported through such filters

## Slide 133: Septic Tank Construction
Septic tanks should be placed on level grade and at a depth that provides adequate gravity flow from home and matches the invert elevation of house sewers.
Septic tanks must be water tight.
RCC and brick are most common construction material.
Other include Plastic, Fiberglass
The Inlet and Outlet devices must be properly positioned and sealed with concrete other adhering material.

## Slide 134: Treatment and Disposal of Septic Tank Sludge and Scum
In Bangladesh, sewerage system is non-existent except for Dhaka, where it covers only about 21 percent of population.
Septic tank (with or without soakage pit) is the predominant method of wastewater disposal in urban areas; direct disposal of wastewater into drains and lowland is also common.
Pit latrines are predominant in low-income urban areas (and throughout the rural areas).
Thus, huge quantities of septic tank sludge as well as fecal sludge (from pit latrines) are produced in urban and rural areas.
Sludge (septic tank/ fecal) is a major source of pollution, and also major source of methane (a greenhouse gas) emission.

## Slide 135: Treatment and Disposal of Septic Tank Sludge and Scum
Septic tank/ fecal sludge should be regularly removed and disposed of in a safe manner. However there is no septic tank sludge treatment/disposal facility in most cities and towns (including in Dhaka).
Consequently, septic tank/ fecal sludge are deposited in lowlands, drains, khals, on road sides, and domestic/ storm sewer lines via manholes.
This hazardous practice promotes spreading of pollution and diseases (and also methane emission).

## Slide 136: Design Problems
(1) Design a septic tank to serve a household of 10 persons, who produce 90 lpcd of wastewater. The tank is to be desludged every 3 years (assume an average temperature of 25 C).

## Slide 137: Disposal of Septic Tank Effluent
Effluent from septic tank is only partially treated, and contains relatively high concentrations of microorganisms, BOD, P, N, etc
It should not be discharged directly into a water body or on land.
"Sub-surface
absorption” is usually
the best method of septic tank effluent disposal

## Slide 138: Soakage Pits
Most commonly used in Bangladesh.
Septic tank effluents flows through pit walls, made of open jointed bricks,
into surrounding soil

## Slide 139: Types of Soakage Pits
Lined Soakage Pit
Unlined Backfilled Soakage Pit

## Slide 140: Soakage Pits (contd.)
Typically soakage pits can be 2.0 to 3.5 m in diameter, and 3 to 6 m deep, depending on amount of wastewater flow, infiltration capacity of soil, and position of groundwater table.
Design principle of soakage pit is same as that for a leach pit (for infiltration)
The soakage pit is usually installed at least 3 m away from the septic tank.

## Slide 141: Design Problems
(1) You have designed a septic tank to serve a household of 10 persons, considering a wastewater flow rate of 90 lpcd and desludging period of 3 years. Now design a soakage pit for the disposal of septic tank effluent. Consider long-term infiltration capacity of soil to be 30 l/m2.day.

## Slide 142: Solution
Effluent flow rate from septic tank, Q = 10 persons x 90 lpcd
= 900 L/day
Infiltration rate, I = 30 l/m2.day
 Area required for infiltration = Q/I = 900 / 30 = 30 m2
Considering circular soakage pit of diameter D and effective depth
L, area available for infiltration = .D.L
 30 m2 = .D.L
Dimensions of soakage pit:
Dia (D) | Depth (L) | Comment
1.25 m | 7.64 m | Consider two pits
1.50 m | 6.37 m | May consider two pits
2.00 m | 4.77 m | 

## Slide 143: Solution
What would be the situation if the soil is compact silty loam with I = 10 l/m2.day
 Area required for infiltration = Q/I = 900 / 10 = 90 m2
 90 m2 = .D.L
Dimensions of soakage pit:
Dia (D) | Depth (L) | Comment
2.00 m | 14.3 m | Need three pits
3.00 m | 9.50 m | Need two pits
3.50 m | 8.20 m | Need two pits
What if population to be served is higher 30 or 50 or 100 (instead of 10 considered in this example)?
Pit size/ number would become unrealistic.
Thus, septic tank system (which depends on infiltration capacity of soil for final disposal of effluent) is not feasible for densely populated urban areas

## Slide 144
Wastewater Collection & Transportation
(Week 14-16)

## Slide 145: Introduction
Most onsite sanitation systems are build relying on the infiltration capacity of soils.
However, as the population densities increase and the per capita water consumption rises due to improvements in the water supply, particularly in the urban centers, on site system often fails because of insufficient land area required for infiltration.
Moreover, soil’s capacity to absorb wastewater with a high organic content also decreases.
Consequently the overflow of the pit latrines or the septic tanks end up in surface water drainage networks causing unsightly, polluted natural streams and rivers.
On-site sanitation systems are like to pollute the groundwater
system when the ground water table is high.

## Slide 146
The obvious alternative to on-site sanitation in such situation is
sewerage, Widely termed as Conventional Sewerage
of a series of underground pipes collecting and
waterborne
System.
It consists transporting
waterborne excreta and other household
wastewater to a distant place.
Some degree of treatment is provided to the wastewater before final disposal into natural watercourses or in some cases onto land.
Unfortunately, conventional sewerage, as currently practiced, is very expensive and is only applicable to cities, commercial, residential and industrial areas which can afford it.
Introduction

## Slide 147: Conventional Sewerage System
The basis functional elements of a conventional sewerage system include the house connection for collections of household or industrial wastewater, a network of sewer systems for collection and conveying the wastewater, a treatment plant for processing the wastewater, and receiving environment (water or land) for disposal of the treated wastewater.
Of the total system, the major investment is made in the collection and conveyance of wastewater through a network of reticulation sewers.

## Slide 148: Important Terms
Wastewater: is the liquid waste conveyed by a sewer and may include domestic and industrial discharges as well as storm sewage, infiltration, and inflow.
Domestic (Sanitary) sewage: is the liquid waste which originates in the sanitary conveniences, e.g., water closets, urinals, baths, sinks, etc. of dwellings, commercial or industrial facilities and institutions. This is sometimes also referred to as black water.
Industrial wastewater: includes the liquid discharges from spent water in different industrial processes such as manufacturing and food processing.
Sullage: is the liquid discharge from kitchens, wash basins etc. and excludes discharge from WCs and urinals. Sullage, also known as grey water, is less foul than domestic sewage and can be discharged through open surface drains in unsewered areas.

## Slide 149
Storm water: is the surface runoff during and immediately after the rainfall, which enters sewers through inlets. Storm water is not as foul as sanitary or industrial sewage and hence can be carried through open drains or channels and disposed of in natural rivers or streams without treatment.
Infiltration: in the water which enters the sewers from the ground through leaks or faulty joints.
Sewer: is a pipe or conduit, generally closed, but normally not flowing full, which carries sewage.
Sanitary sewer: carries sanitary sewerage and is designed to exclude storm sewage, infiltration, and surface inflow. Industrial waste may be carried in sanitary sewers, depending upon its characteristics.
Strom sewer: carries storm sewage and any other waste which may be discharged into streets or onto the surface of the ground.
Sewerage: refers to the entire system of collection, treatment and disposal of sewage through a system of reticulation sewers.
Important Terms

## Slide 150: Functional Elements of a Sewerage System
The essential functions of a sewerage system include:
Collection and conveyance;
Treatment; and iii) Disposal
Collection refers to the collection of sewage from different points of generation and conveying sewage to any desired points through a network of sewers.
Sewage treatment includes any process which may be used to modify the characteristics of sewage.
Sewage disposal refers to the discharge of liquid waste to the environment. Normally, but not always, disposal implies some degree of treatment prior to discharge.

## Slide 151: Types of Collection Systems
Separate sewerage consists in the separate collection of municipal wastewaters (black water from toilets, grey water and industrial wastewater) and surface run-off (rainwater and storm water).
The separate collection prevent the overflow of sewer systems and treatment stations during rainy periods and the mixing of the relatively little polluted surface run-off with chemical and microbial pollutants from the municipal wastewater.

## Slide 152
•
•
•
•
•
•
•
•
•
•

## Slide 153
Convenience
Less maintenance
Grey water and possibly storm water can be managed concurrently
Can handle large volumes of flow
No problems related to discharging industrial wastewater

## Slide 154
Very high capital costs; high operation and maintenance costs
A minimum velocity must be maintained to prevent the deposition of solids in the sewer
Difficult and costly to extend as a community changes and grows
Difficult to construct in high-density areas, difficult and costly to
maintain

## Slide 156: Partially Separate System
A partially separate system is a modification of the separate system in which the separate sewer discharging domestic sewage and industrial wastes also contain a portion of the surface drained from back-paved yards and roofs of the house.
Advantages
It provides reasonable sizes of sewers and is economical.
The rainwater provides some safeguard against silting in the sewer.
Disadvantages
Low velocity during the dry period.
Storm overflows may be found necessary.

## Slide 157: Assignment
Suitable Conditions for choosing a specific type of sewerage system

## Slide 158
Types of Sewer: The types and sizes of sewers vary with size of the collection system and the location of the wastewater treatment facilities. The principal types of sewers found in most collection systems are as follows:
Building sewers: also called house connection, are used to convey wastewater from the building to lateral or branch sewers, or any other sewer except another building sewer. Building sewers normally begin outside the building.
Lateral or branch sewer: Lateral sewers from the first element of a community sewage collection system and are usually in streets. They are used to collect sewage from one or more building sewers and convey it to a main sewer.
Main sewer: Main sewers are used to convey sewage from one or more lateral sewers to trunk sewers or to interceptor sewers.
Trunk sewers: These are large sewers that are used to convey sewage from main sewers to treatment plants or their disposal facilities or to larger intercepting sewers.
Intercepting sewers: These are large sewer that are used to intercept number of main or
trunk sewers and convey the wastewater to treatment or other disposal facilities.
Outfall sewers: These are the lengths of main or trunk or interceptor sewers which lie between connections and the final point of disposal or treatment plant.

## Slide 159: Small Bore Sewerage System In order to extend adequate sanitation services to medium to low-income communities, small bore sewerage (SBS) system is introduced. This is a recent sanitation technology that offers all the advantages of conventional waterborne sewerage systems but at a much lower cost than the conventional ones.
SBS system elements:
There are three elements to a small bore sewerage system.
These are-
Septic tanks;
Small bore sewer network; and
Treatment plant.

## Slide 160
The SBS system collects wastewater discharges from all the fixtures in households (or other premises) in a similar fashion to the conventional sewerage system. The basic difference between the two systems is the incorporation of septic tanks within the individual premises as part of the SBS system. The wastewater collected in the septic tank is then transported under gravity through a network of reticulation sewers to a treatment plant comprising a series of stabilization lagoons
In the case of an existing septic tank system the sewer installation commences immediately downstream of the existing septic tank, and new developments must install septic tanks to be able to connect to the SBS system.

## Slide 161
Thanks for Your Attention!!!