## Slide 1: CE 0732-2201 Structural Analysis and Design-I
Prepared By-
Md. Rejoan Chowdhury
Lecturer
Dept. of Civil Engineering
University of Global Village (UGV), Barishal

## Slide 2
Structural Analysis and Design-I
COURSE CODE: CE 0732-2201 CREDIT: 04
MID EXAMINATION: 2 HOURS CIE MARKS: 120
SEMESTER END EXAMINATION: 3 HOURS SEE MARKS: 80
Course Learning Outcomes (CLOs): After completing this course, students will be able to-
CLO 01 Understand the concepts and fundamentals of truss structures.
CLO 02 Analyze two hinged and three hinged arches.
CLO 03 Determine maximum moment at mid-span for wheels.
CLO 04 Assess the deflection of beams applying unit load method.
CLO 05 Analyze lateral loads for building such as wind force and earthquake load.

## Slide 3
Sl. | Course Contents | Hours | CLOs
1 | Definition of trusses, characteristics, advantage and uses, types of trusses, assumptions, components, zero force members, Connections, supports, truss analysis (method of section and joint), objectives, possibility of trusses being curved members, examples of trusses. | 4 | CLO 1
2 | Definition, advantages and disadvantages of two hinged arches, mathematical problems. | 6 | CLO 2
3 | Definition, advantages and disadvantages of three hinged arches, mathematical problems. | 6 | CLO 2
4 | Definition and importance of wheel load analysis, theorem of wheel load analysis, mathematical problems. | 4 | CLO 3
5 | Theorem of beam deflection, mathematical problems. | 6 | CLO 4
6 | Types of load, exposures, sustained wind pressure, design wind pressure, design base shear, distribution of lateral loads (wind and earthquake). | 6 | CLO 5

## Slide 4
Week | Topic | Teaching Learning Strategy | Assessment Strategy | CLOs | Page No.
1-2 | Introduction and basic concepts of truss structures. | Lecture, Discussion | Project, Mid, Final | CLO 1 | 06-27
3-5 | Two hinged arches. | Lecture, Discussion | Assignment, Mid, Final | CLO 2 | 28-36
6-8 | Three hinged arches. | Lecture, Discussion | Assignment, Class Test, Mid, Final | CLO 2 | 37-63
9-10 | Wheel load analysis. | Lecture, Discussion | Assignment, Class Test, Mid, Final | CLO 3 | 64-81
11-13 | Deflection of beam. | Lecture, Discussion | Assignment, Class Test, Final | CLO 4 | 82-92
14-16 | Lateral load analysis | Lecture, Discussion | Assignment, Final | CLO 5 | 93-116
References
1. Theory of Simple Structures - Thomas Shed & Jamison Vawter 2. Elementary Structural Analysis - Charles Norris & John Wilbur

## Slide 5
Bloom’s Category Marks (out of 120) | Tests (60) | Assignments (20) | Quizzes (20) | External Participation in Curricular/Co-Curricular Activities (20)
Remember | 10 |  | 10 | Attendance 20
Understand | 10 |  | 10 | 
Apply | 10 |  |  | 
Analyze | 10 |  |  | 
Evaluate | 10 |  |  | 
Create | 10 | 20 |  | 
Bloom’s Category | Tests
Remember | 10
Understand | 15
Apply | 15
Analyze | 15
Evaluate | 15
Create | 10
ASSESSMENT PATTERN
CIE-Continuous Internal Evaluation (120 Marks)
SEE- Semester End Examination (80 Marks)

## Slide 6
Introduction & Basic Concepts of Trusses
(Week 1-2)

## Slide 7: Introduction
What are the trusses?
Trusses are framework structures that distributes the loads by taking advantage of the inherent stability of a triangle.
They are designed to sustain inclined, vertical, horizontal loads accruing at or between its points of support.

## Slide 8: Characteristics of Trusses
The general configuration of a truss is triangle.
The members are connected of their end by frictionless pin.
The loads are applied only at joints and not at the intermediate points of a member.

## Slide 9: Advantages & Uses of Trusses
Trusses enables the creation of light structures that can span large distances and endure heavy loads.
Their presence enables builders to achieve maximal economy of materials.
They are generally used in roofs, bridges and buildings.
They are also used in structures for architectural purposes.

## Slide 10: Types of Trusses
Fig.: Simple Truss
Fig.: Compound Truss
Fig.: Complex Truss

## Slide 11: Types of Roof Trusses
Fig.: Pratt Truss
Fig.: Howe Truss

## Slide 12: Types of Roof Trusses
Fig.: Bow String Truss
Fig.: Three-Hinged Arch (Truss)

## Slide 13
Fig.: Warren Fink Truss
Fig.: Fan Fink Truss
Types of Fink Trusses

## Slide 14: Assumptions of Trusses
All loads are transmitted at joints.
All members are joined by pin connections.
Consist entirely of two-force members.
Can contain zero-force member.

## Slide 15: Zero-force Members
What are zero-force members?
Structural members that carry no force.
Why do we use them?
Used to provide stability-
  During construction,
  If (intermittent) loading of the truss changes.
Shortens chord length and increases buckling capacity of compression members.

## Slide 16: Components of Trusses
Figure: Components of a Typical Truss

## Slide 17: Joint Connections of Trusses
Fig.: Welded Connection
Fig.: Pin Connection
Fig.: Gusset Plate Connection

## Slide 18: Truss Supports
Fig.: Fixed Support
Fig.: Roller Support

## Slide 19: Working with Trusses: Analysing Structural Forces in Truss Members
Truss members will carry either
  Axial tension (T) forces or
  Axial compression (C) forces.
There are two methods of evaluating trusses.
  Method of Joints (static equilibrium of a point)
  Method of Sections (static equilibrium of a rigid body).

## Slide 20: Truss Analysis: Method of Joints
Evaluate an individual joint or pin connection.
Treat each joint as a 2D particle in equilibrium.
Can have a maximum of two unknowns.
Can sum forces in x & y direction.

## Slide 21: Truss Analysis: Method of Sections
Evaluate a section including multiple joints.
Treat as 2D rigid body in equilibrium.
Must cut through structural members to evaluate the force.
Maximum of three unknowns (to solve everything).
Can sum forces in x & y direction.
Can sum moments.

## Slide 22: So, What Are The Objectives of Truss Analysis?
The prime objectives are –
-To determine the support reactions.
-To determine the forces supported by individual members of the truss.

## Slide 23: Can trusses have curved members?
The ideal answer is NO.
But, if the members are sufficiently stiff so that moments developed at the connections are negligible, the answer can be yes.
The most notable thing is, Curved members are not so cost-effective.

## Slide 24: Some Cool Examples of Truss Structures (Bangladesh)
Bhairab Railway Bridge (UK-Bangladesh Friendship Bridge-constructed)

## Slide 25: Some Cool Examples of Truss Structures (Bangladesh)
Padma Bridge
Hardinge Railway Bridge

## Slide 26: Some Cool Examples of Truss Structures (Overseas)

## Slide 27: Some Cool Examples of Truss Structures (Overseas)
Waterville Bridge USA

## Slide 28: ‘Arches' (Two Hinged Arch) (Week 3-5)
28

## Slide 29: Introduction
In case of beams supporting uniformly distributed load, the maximum bending moment increases with the square of the span and hence they become uneconomical for long span structures. In such situations arches could be advantageously employed, as they would develop horizontal reactions, which
in turn reduce the design bending moment.
Figure 1: Beam and Arch comparison
2
29

## Slide 30
For example, in the case of a simply supported beam shown in Figure 1, the bending moment below the load is 3PL/16.
Now consider a two hinged symmetrical arch of the same span and subjected to similar loading as that of simply supported beam. The vertical reaction could be calculated by equations of statics. The horizontal reaction is determined by the method of least work. Now the bending moment below the load is (3PL/16 − Hy).
It is clear that the bending moment below the load is reduced in the case of an arch as compared to a simply supported beam.
It is observed that, the cable takes the shape of the loading and this shape is termed as funicular shape.
If an arch will constructed in an inverted funicular shape then it would be subjected to only compression for those loadings for which its shape is inverted funicular.
30

## Slide 31
Figure 2: Cable and Arch structure
Since in practice, the actual shape of the arch differs from the inverted funicular shape or the loading differs from the one for which the arch is an inverted funicular.
Arches are also subjected to bending moment in addition to compression.
As arches are subjected to compression, it must be designed to resist buckling.
31

## Slide 32
Figure 3: (a) Arch (b) Beam
A structure is classified as an arch not based on its shape but the way it supports the lateral load. Arches support load primarily in compression.
For example in Figure 3(b), no horizontal reaction is developed. Consequently bending moment is not reduced. It is important to appreciate the point that the definition of an arch is a structural one, not geometrical.
32

## Slide 33
6
For large spans like bridges, arches are provided in stead of beams. Arches are curved beams that transfer loads to their planes.
Arches transfer loads to abutments at springing points. Hinges may be provided at springing points.
The top most point is called crown.
The height of the crown above support level is called rise.
Figure 4: Typical arch bridges
33

## Slide 34
7
Due to curved nature of arches, they give rise to horizontal forces.
Abutments are designed for horizontal forces also.
Any section in the arch is subjected to normal thrust, radial shear and bending moment.
Loads in the arches partly transferred by axial compression and partly by flexure.
Figure 5: Arch with section showing forces
34

## Slide 35: Types of Arches
There are mainly three types of arches that are commonly used in practice:
Three hinged arch,
Two-hinged arch
Fixed-fixed arch or Hingeless arch
Three-hinged arch is statically determinate structure and its reactions / internal
forces are evaluated by static equations of equilibrium.
Two-hinged arch and fixed-fixed arch are statically indeterminate structures. The indeterminate reactions are determined by the method of least work or by the flexibility matrix method.
8
35

## Slide 36
a) Three – hinged arch
b) Two - hinged arch
c) Fixed – Fixed arch
Figure 6: Types of arches
9
36

## Slide 37: ‘Arches' (Three Hinged) (Week 6-8)
37

## Slide 38: Introduction to Three Hinged Arch
Three hinged arches is statically determinate structure and its reaction and internal forces are evaluated by static equations of equilibrium.
Arches transfer loads to abutments at springing points.
The horizontal distance between one support to another support is called span.
The Top most point of the arch is called crown.
The height of the crown above the support level is called rise.
Figure 1:Three-hinged arch
2
38

## Slide 39: Types of three-hinged arches
There are two types of three-hinged arches according to the shape of the structure.
Circular three-hinged arch
Parabolic three-hinged arch
Circular three-hinged arch
From the property of a circle, the radius ‘R’ of the circular arch of span ‘L’ and rise ‘h’
39

## Slide 40: Circular three-hinged arch
Taking ‘A’ as origin at support, the coordinates of any point ‘D’ on the arch is:
Figure 2: Coordinates of ‘D’
40

## Slide 41: Parabolic three-hinged arch
In the case of a parabolic arch, taking the springing point as the origin its
𝐿2
equation = y = 4ℎ𝑥(L-x)
𝑦
2
If the crown is taken as the origin, the equation of the parabolic curve = 𝑥 = a,
where a = Constant
Figure 3: Parabolic arch with origin at ‘A’
41

## Slide 42: If the springing point are at the same level:
Figure 4: Parabolic arch with origin at crown
6
42

## Slide 43: If the springing points are not at the same level:
Let h1 and h2 is the depth of the abutments from the crown and let ‘L’
is the span.
Applying this equation to
points A and B, we get
Constant
Figure 5: Parabolic arch with springing at different level
7
43

## Slide 44: Analysis for Static Loads
Consider a three-hinged arches as shown in Figure 6.
The ends are hinged there is two reaction components at each end namely vertical and horizontal.
There are four reaction components i.e. VA, HA, VB and HB.
Figure 6: Three-hinged arch with load
8
44

## Slide 45: ∑FH = 0
For any plane structure, there are three independent equilibrium equations, i.e.
∑FV = 0
MA or MB = 0
In this case, the fourth equation is Mc = 0, since C is a hinge
If horizontal load is not acting, HA = HB = H
In this case the following equations are used
∑FV = 0
MC = 0
9
45

## Slide 46
Now, consider a section at D
Let V = Vertical shear, Q = Radial shear, N = Normal thrust
Figure 7: Internal forces at D
In the above Figure 7, All these forces are indicate positive sign, The normal thrust and radial shear is calculated by
N = V sin θ + H cos θ
Q = V cos θ – H sin θ
10
46

## Slide 47: Three-Hinged Arches Solved Problems
47

## Slide 48: Q1. A three-hinged circular arch hinged at the springing and crown points has a span of 40 m and a central rise of 8 m. It carries a uniformly distributed load 20 kN/m over the left-half of the span together with a concentrated load of 100 kN at the right quarter span point. Find the reactions at the supports, normal thrust and shear at a section 10 m from left support.
Figure 1
2
48

## Slide 49
First find the reactions by using equilibrium equations.
By taking moment about B and equate to zero i.e. ∑MB = 0
VA × 40 - 20× 20 × 30 – 100 × 10 = 0
VA = 325 kN
Summation of vertical force is zero i.e. ∑FV = 0
VA + VB = 20 × 20 + 100
VB = 500 – 325 = 175 kN
Since, C is hinged, at hinge MC = 0 (Take moment for right portion or left portion of hinge and equate the moment to zero, and find H)
VB × 20 – 100 × 10 – H × 8 = 0
175 × 20 – 100 × 10 – H × 8 = 0
H = 312.5 kN
49

## Slide 50
Let D be the point 10 m from the left support where the normal thrust and radial
shear are to be found. Now from the property of circles.
Vertical shear at D, V = VA – 20 × 10
V = 325 – 200 = 125 kN
Normal thrust at D, N = V sin θ + H cos θ
N = 125 sin 29.171̊ + 312.5 cos 20.171̊ = 336.437 kN
Radial shear at D,
Q = V cos θ – H sin θ
Q = 125 cos 20.171̊ - 312.5 sin 20.171̊ = 9.575 kN
50

## Slide 51
Q2. A circular arch to span 20 m with a central rise 5 m is hinged at the crown and springing. It carries a point load of 100 kN at 6 m from the left support. Calculate 1) The reactions at the supports, 2) The reactions at crown, 3) Moment at 5 m from the left support.
Figure 1
51

## Slide 52
First find the reactions using equilibrium equations
Taking the moment about B, we get VA × 25 = 100 × (25 – 6) VA = 76 kN
Taking summation of vertical force is zero (∑V = 0), we get
VA + VB = 100
VB = 100 – 76 = 24 kN
For horizontal reaction, taking moment about C, we get 24 × 12.5 – H × 5 = 0
H = 60 kN
52

## Slide 53
Considering the equilibrium of the left half of the arch, the reaction at crown can be found from Figure 2.
Correct direction of VC = 24 kN
Figure 2
By taking summation of horizontal force zero, H = 60 kN ( )
By taking summation of vertical force zero,
76 – 100 – VC = 0
VC = 76 -100 = -24 kN = 24 kN (upward direction) ( )
53

## Slide 54: Moment at 5 m from the left support:
From the property of circle, we get
H (2R – h) = 𝐿 × 𝐿
2 2
5 (2R – 5) = 25 × 25
2 2
R = 18.125 m
From Figure 1, we can find, R sin θ = 12.5 – 5 = 7.5
sin θ =
7.5
18.125
= 0.4138
θ = 24.443̊
yD = h – R (1 – cos θ) = 5 – 18.125 (1 – cos 24.443̊)
yD = 3.375 m
Moment at D = MD = VA × 5 – H × yD
MD = 76 × 5 – 60 × 3.375 = 177.5 kNm
8
54

## Slide 55
Q3. A three-hinged parabolic arch hinged at the supports and at the crown has a span of 24 m and a central rise of 4m. It carries a concentrated load of 50 kN at 18 m from left support and a uniformly distributed load of 30 kN/m over the left half portion. Determine the moment, thrust and radial shear at a section 6 m from the left support.
Figure 1
9
55

## Slide 56
First find the Reactions, By taking moment about B, we get
VA× 24 – 30 × 12 × 18 – 50 × 6 = 0
VA = 282.50 kN
Then by taking summation of vertical force is zero, we get
VA + VB = 30 × 12 + 50
VB = (30 × 12 + 50) – 282.50 = 127.5 kN
By taking moment about crown C is zero (Right half)
VB × 12 – H × 4 – 50 × 6 = 0
127.5 × 12 - H × 4 – 50 × 6 = 0
H = 307.5 kN
10
56

## Slide 57
Moment at a distance 6 m from the left support,
MD = VA
D
2
× 6 – H × y – 30 × 6
2
D
242
In the parabolic arch,
y = 4ℎ𝑥 (𝐿 −𝑥)
𝐿2
Therefore, at x = 6 m,
y = 4×4×6(24−6) = 3 m
D
2
M = 282.5 × 6 – 307.5 × 3 – 30 × 6
2
MD = 232.5 kNm
Vertical shear at D,
VD = VA – 30 × 6
VD = 282.5 – 30 × 6 = 102.5 kN
11
57

## Slide 58
𝑑𝑥
To find the θ, differentiating y with respect to x
𝑑𝑦 = tan θ = 4ℎ(𝐿−2𝑥)
𝐿2
Therefore, at x = 6 m, tan θ =
4×4(24−2×6)
24×24
θ = 18.435̊
Normal thrust = N = V sin θ + H cos θ
N = 102.5 sin 18.435̊ + 307.5 cos 18.435̊
N = 324.133 kN
Radial shear = Q = V cos θ – H sin θ
Q = 102.5 cos 18.435̊ - 307.5 sin 18.435
Q = 0
12
58

## Slide 59: Q4. show that the parabolic shape is a funicular shape for a three hinged arch subjected to a uniformly distributed load over to its entire span.
Figure 1
13
59

## Slide 60
Let the span of the arch be L and rise be h as shown in Figure.
1
Due to symmetric loading, VA = VB = 2 × total load
VA = VB
= 1
× w × L = 𝑤𝐿
2 2
Taking moment about C, we get (Left side of the hinge C)
C A
2 2 4
M = V × 𝐿 - H × h – w × 𝐿 × 𝐿 = 0
2
𝑤𝐿 × 𝐿 - H × h - 𝑤𝐿 = 0
2 2 8
2
H = 𝑤𝐿
8
14
60

## Slide 61
Moment at any section distance x from A,
A
M = V × x – H × y - 𝑤𝐿2
2
But in a parabolic arch,
y = 4ℎ𝑥(𝐿−𝑥)
𝐿2
M =
2 8
𝐿2
2 2
𝑤𝐿 𝑥 - 𝑤𝐿 × 4ℎ𝑥(𝐿−𝑥) - 𝑤𝐿
2
M =
𝑤𝐿𝑥
𝑤𝐿2
2 2 2
- 𝑤x(L-x) - = 0
Thus, for a parabolic arch subjected to a uniformly distributed load over its entire span, the bending moment at any section is zero.
Hence, the parabolic shape is a funicular shape for a three hinged arch subjected to uniformly distributed load over entire span.
15
61

## Slide 62
The arch is shown in Figure 1.
For getting reaction, taking moment about B and equate to zero (∑MB = 0), gives
VA × 36 – 120 (36 – 12) = 0
VA = 80 kN
By taking summation of vertical force zero (∑V = 0)
VA + VB = 120
VB = 120 – 80 = 40 kN
Beam moment diagram is a triangle with maximum ordinate at the load point can be found by
Beam moment at load point =
120×12(36−12)
36
= 960 kNm
Note: For simply supported beam of length L with eccentrically loading (W), at a distance a from support A and b from support B, Maxm. BM at load point = Wab/L (use this in above calculation)
17
62

## Slide 63
The beam moment is drawn first as shown in Figure 2.
We know at mid span the net bending moment is zero
The ordinate of the beam moment diagram at mid span can be calculated by
24
two similar triangle = 960×18 = 720 kNm
Since, MC = 0 in the arch, Hh = 720 kNm
or H = 720 = 720 kN = 120 kN
ℎ 6
A parabola is drawn with its central ordinate equal to 720 kNm as shown in
Figure 2.
The equation of the parabola is
y
BM
= H × y = H × 4ℎ𝑥(𝐿−𝑥)
𝐿2
18
63

## Slide 64
Wheel Load
(Week 9-10)

## Slide 82
Deflection By
Unit Load Method
(Week 11-13)

## Slide 93
Lateral Load Analysis
(Week 14-16)