## Slide 1
University of Global Village (UGV), Barishal
Mechanics of Solids-I
Content of Theory Course
Program: B.Sc. in CE
Prepared By
Rubieyat Bin Ali
Assistant Professor & HOD
Department of Civil Engineering
University of Global Village (UGV), Barishal

## Slide 2
Course Title | Mechanics of Solids-I
Course Code | CE 0732-2205
Credits | 03
CIE Marks | 90
SEE Marks | 60
Exam Hours | 2 hours (Mid Exam) 3 hours (Semester Final Exam)
Level | 4th Semester
BASIC COURSE INFORMATION

## Slide 3
Course Code: CE 0732-2205 | CREDIT:03
 | TOTAL MARKS:150
Mid Exam Hours 2 | CIE MARKS: 90
Semester End Exam Hours 3 | SEE MARKS: 60
Mechanics of Solids-I
CLO 1 | Understand the types of loads and stresses in different loaded members and develop skills to determine them.
CLO 2 | Identify the magnitude of safe loads and stresses to operate individual members and structures without failure.
CLO 3 | Perform structural design by determining the value of shear force and bending moment at a given point for structural members such as a beam, column, frame, etc.
CLO 4 | Assess the deflections and deformations of loaded flexural members.
Course Learning Outcomes (CLOs): After completing this course successfully, the students will be able to-
Course Teacher: Rubieyat Bin Ali

## Slide 4
SL | Content of Course | Hrs | CLOs
1 | Introduction and analysis of supports and connections: Roller support, hinged/pinned support, fixed support and simple support. | 8 | CLO1
2 | Introduction and analysis of internal forces: Tension, compression, axial stress, strain, shear stress, shear force, bending moment, deformation, stress-strain diagram, elasticity, rigidity, yield strength, ultimate strength, strain hardening, strain softening, elastic limits, plastic limit, fracture point, ductility, engineering stress-strain, true stress-strain, bone shear failure, hardness, brittleness, resilience and toughness. | 8 | CLO1, CLO2
3 | Definition of some mechanical properties of materials: Poisson’s ratio, definition of torque and torsion, stresses in thin walled pressure vessels: hoop and longitudinal stress, Introduction to different types of loading and supports. | 9 | CLO2, CLO3
4 | Shear force and bending moment diagram under different conditions: Roller, hinged, fixed support, uniformly distributed and varying load, inclined load and special frame, Slope and deflection of beams, elastic curve, method of area moment and double integration. | 9 | CLO3, CLO4
Text Book:
Strength of Materials (4th ed.). Pytel, A. & Singer, F. L., Harper Collins Inc., 1987; ISBN: 0-06-350599-1
Mechanics of Materials. Beer and Johnston; McGraw- Hill, 2009; ISBN: 0073529389
Mechanics of Materials (9th ed.). Hibbeler, R. C., Pearson Prentice Hall, 2014; ISBN: 10: 0-13-3254429

## Slide 5
ASSESSMENT PATTERN
CIE- Continuous Internal Evaluation (90 Marks)
SEE- Semester End Examination (60 Marks)
Bloom’s Category | Tests
Remember | 10
Understand | 10
Apply | 10
Analyze | 15
Evaluate | 10
Create | 5
Bloom’s Category Marks (out of 90) | Tests (min 4) (45) | Assignments (min 4) (15) | Quizzes (15) | External Participation in Curricular/Co-Curricular Activities (15)
Remember | 10 |  | 10 | Attendance/Field Visit/Presentation/Project Exhibition (15)
Understand | 5 |  | 5 | 
Apply | 10 |  |  | 
Analyze | 10 |  |  | 
Evaluate | 5 |  |  | 
Create | 5 | 15 |  | 

## Slide 6
Week | Topic | Teaching-Learning Strategy | Assessment Strategy | Corresponding CLOs
1 | Definition of support and connection, Importance of connection | Lecture, discussion, group work | Quiz, Written Exam | CLO1
2 | Details of roller support, Details of hinged/pinned support or connection | Oral Presentation, debate | Assignment, Written, Quiz | CLO1
3 | Fixed and simple support | Video lecture, Field visit | Report writing, Demonstration | CLO1
4 | Tension, compression, axial stress, strain, Shear stress, shear force, bending moment, deformation | Lecture | Viva, Quiz | CLO1, CLO2
5 | Tensile stress-strain diagram | Project exhibition | Project, Field visit | CLO2
6 | Elasticity, rigidity, yield strength, ultimate strength, Elastic limits, plastic limit and fracture point, Strain hardening and strain softening properties | Discussion, Video Presentation | Quiz, Written Exam | CLO2
7 | Details of ductility, True stress-strain Diagram, Bone shear failure | Case-based Learning, Demonstration | Assignment, Written, Quiz | CLO2
8 | Hardness and brittleness, Resilience and toughness, Poisson’s ratio and torque | Lecture, discussion, group work | Report writing, Demonstration | CLO2
9 | hoop stress and longitudinal stress | Oral Presentation, debate | Viva, Quiz | CLO2
10 | SFD and BMD for Roller support, BMD for hinged and fixed support | Video lecture | Project, Field visit | CLO3
Course plan specifying content, CLOs, teaching learning and assessment strategy mapped with CLOs

## Slide 7
Week | Topic | Teaching-Learning Strategy | Assessment Strategy | Corresponding CLOs
11 | BMD for uniformly distributed load, varying load and inclined load | Lecture | Quiz, Written Exam | CLO3
12 | BMD for frame structure, free moment and link | Project exhibition | Assignment, Written, Quiz | CLO3
13 | BMD for large continuous beam and cantilever beam, Two degree area calculation | Discussion, Video Presentation | Report writing, Demonstration | CLO13
14 | Distance determination from two degree area and similar triangle | Case-based Learning, Demonstration | Viva, Quiz | CLO3
15 | Slope and deflection of beams and Elastic curve | Lecture, discussion, group work | Project, Field visit | CLO4
16 | Double integration method and Area moment method | Oral Presentation, debate | Quiz, Written Exam | CLO4
17 | Practice and Exercise, Practice and Exercise, Practice and Exercise | Video lecture | Assignment, Written, Quiz | CLO3, CLO4
Course plan specifying content, CLOs, teaching learning and assessment strategy mapped with CLOs

## Slide 8
Week 1
Pages 9-13
Support and Connections

## Slide 9
Support and Connections: Definition
In civil engineering, supports and connections are critical components of a structure that ensure its stability and safety:
Supports
Points or areas of a structure that connect to the ground or other elements to transfer forces. Supports can be located at the ends, midpoints, or other intermediate points of a structural element. The type of support determines the type of load it can resist.
Connections
The way a built structure joins to its foundation. Connection detailing is important in both steel and concrete structures, but the details differ based on the material properties.

## Slide 10
Main Key Factors of Support and Connection in Civil Engineering Point of view
Distributing loads: Supports distribute loads and pressures from the structure to the ground.
Limiting deflection: Supports limit the deflection of a structure.
Decreasing vibrations: Supports decrease vibrations in a structure.
Load bearing capacity: The type of support connection affects the load bearing capacity of each element in the structure.

## Slide 11
Importance
Structural systems transfer their loading through a series of elements to the ground.
This is accomplished by designing the joining of the elements at their intersections. Each connection is designed so that it can transfer, or support, a specific type of load or loading condition. In order to be able to analyse a structure, it is first necessary to be clear about the forces that can be resisted, and transferred, at each level of support throughout the structure. The actual behaviour of a support or connection can be quite complicated. Structural steel systems have either welded or bolted connections. Precast reinforced concrete systems can be mechanically connected in many ways, while cast-in-place systems normally have monolithic connections. Timber systems are connected by nails, bolts, glue or by engineered connectors. No matter the material, the connection must be designed to have a specific rigidity.

## Slide 12
Support and Connections: Types
The three common types of connections which join a built structure to its foundation are; roller, pinned and fixed. A fourth type, not often found in building structures, is known as a simple support. This is often idealized as a frictionless surface). All of these supports can be located anywhere along a structural element. They are found at the ends, at midpoints, or at any other intermediate points. The type of support connection determines the type of load that the support can resist. The support type also has a great effect on the load bearing capacity of each element, and therefore the system.

## Slide 13
Support and Connections: Reactions
In engineering mechanics, support reactions are forces and moments exerted by the supports or connections that hold a structure or mechanical system in equilibrium. These reactions are critical for analysing and designing structures, as they determine how external loads are distributed within the system.

## Slide 14
Week 2
Pages 15-18
Support and Connections

## Slide 15
ROLLER SUPPORTS
Roller supports are free to rotate and translate along the surface upon which the roller rests. The surface can be horizontal, vertical, or sloped at any angle. The resulting reaction force is always a single force that is perpendicular to, and away from, the surface. Roller supports are commonly located at one end of long bridges. This allows the bridge structure to expand and contract with temperature changes. The expansion forces could fracture the supports at the banks if the bridge structure was "locked" in place. Roller supports can also take the form of rubber bearings, rockers, or a set of gears which are designed to allow a limited amount of lateral movement.
Figure: Roller Support

## Slide 16
ROLLER SUPPORTS
A roller support cannot provide resistance to a lateral forces. Imagine a structure (perhaps a person) on roller skates. It would remain in place as long as the structure must only support itself and perhaps a perfectly vertical load. As soon as a lateral load of any kind pushes on the structure it will roll away in response to the force. The lateral load could be a shove, a gust of wind or an earthquake. Since most structures are subjected to lateral loads it follows that a building must have other types of support in addition to roller supports.
Figure: Roller Support

## Slide 17
PINNED SUPPORTS/CONNECTIONS
A pinned support can resist both vertical and horizontal forces but not a moment. They will allow the structural member to rotate, but not to translate in any direction. Many connections are assumed to be pinned connections even though they might resist a small amount of moment in reality. It is also true that a pinned connection could allow rotation in only one direction; providing resistance to rotation in any other direction
Figure: Pinned Connection

## Slide 18
PINNED SUPPORTS/CONNECTIONS
The knee can be idealized as a connection which allows rotation in only one direction and provides resistance to lateral movement. The design of a pinned connection is a good example of the idealization of the reality. A single pinned connection is usually not sufficient to make a structure stable. Another support must be provided at some point to prevent rotation of the structure. The representation of a pinned support includes both horizontal and vertical forces.
Figure: Pinned Connection

## Slide 19
Week 3
Pages 20-22
Support and Connections

## Slide 20
FIXED SUPPORTS
Fixed supports can resist vertical and horizontal forces as well as a moment. Since they restrain both rotation and translation, they are also known as rigid supports. This means that a structure only needs one fixed support in order to be stable. All three equations of equilibrium can be satisfied. A flagpole set into a concrete base is a good example of this kind of support. The representation of fixed supports always includes two forces (horizontal and vertical) and a moment.
Figure: Fixed Support

## Slide 21
SIMPLE SUPPORTS
Simple supports are idealized by some to be frictionless surface supports. This is correct in as much as the resulting reaction is always a single force that is perpendicular to, and away from, the surface. However, are also similar to roller supports in this. They are dissimilar in that a simple support cannot resist lateral loads of any magnitude. The built reality often depends upon gravity and friction to develop a minimal amount of frictional resistance to moderate lateral loading.
Figure: Simple Support

## Slide 22
SIMPLE SUPPORTS
For example, if a plank is laid across gap to provide a bridge, it is assumed that the plank will remain in its place. It will do so until a foot kicks it or moves it. At that moment the plank will move because the simple connection cannot develop any resistance to the lateral load. A simple support can be found as a type of support for long bridges or roof span. Simple supports are often found in zones of frequent seismic activity.
Figure: Simple Support
Lecture Courtesy: Massachusetts Institute of Technology (MIT)

## Slide 23
Week 4
Pages 24-31
Basic Materials Properties

## Slide 24
Tension and Compression
Tension and compression are forces that act on materials, causing them to stretch or squeeze in different ways:
Tension
A pulling or stretching force that causes a material to elongate or deform. Tension is often referred to as positive stress.
Compression
A pushing or squeezing force that causes a material to shorten or deform. Compression is often referred to as negative stress.

## Slide 25
Axial Stress and Strain
Stress can be defined by ratio of the perpendicular force applied to a specimen divided by its original cross sectional area, formally called engineering stress. To compare specimens of different sizes, the load is calculated per unit area, also called normalization to the area. Force divided by area is called stress. In tension and compression tests, the relevant area is that perpendicular to the force. In shear or torsion tests, the area is perpendicular to the axis of rotation. The stress is obtained by dividing the load (F) by the original area of the cross section of the specimen ().

## Slide 26
Axial Stress and Strain
Strain is the ratio of change in length due to deformation to the original length of the specimen, formally called engineering strain. strain is unit less, but often units of m/m (or mm/mm) are used.
The strain used for the engineering stress-strain curve is the average linear strain, which is obtained by dividing the elongation of the gage length of the specimen, by its original length.

## Slide 27
Shear Stress
Tensile and compressional stress can be defined in terms of forces applied to a uniform rod.
Shear stress is defined in terms of a couple that tends to deform a joining member.

## Slide 28
Shear force definition
Shear force is a force acting in a direction that's parallel to a surface or cross section of a body. The word shear in the term is a reference to the fact that such a force can cut, or shear, through the surface or object under strain. In solid mechanics, shearing forces are unaligned forces pushing one part of a body in one specific direction, and another part of the body in the opposite direction. When the forces are collinear (aligned into each other), they are called compression forces.
Cross-section
Longitudinal direction

## Slide 29
Shear force example
Example: Cutting bread, Cutting paper, beam bending, drawing picture, sliding cash note, painting, brushing teeth, bone shear failure etc.
Figure: Shear force example

## Slide 30
Bending Moment
Bending moment is the internal resistance of a structural element to bending when an external force is applied. It's a measure of the effect of a load that causes a structural member to bend.
Bending moment = Force x Distance
Figure: Bending moment
Deformation
In civil engineering, deformation is the change in shape or size of an object due to an applied force or change in temperature.

## Slide 31
Figure: Different types of loading condition in material.

## Slide 32
Week 5
Pages 33
Basic Materials Properties

## Slide 33
Figure: Tensile stress-strain diagram of reinforcement.

## Slide 34
Week 6
Pages 35-38
Basic Materials Properties

## Slide 35
A tensile stress-strain diagram, also known as a stress-strain curve, illustrates the relationship between a material's stress and strain. The curve can be used to determine a material's characteristic values, such as its elastic behavior and tensile strength.
Some properties of a tensile stress-strain diagram include:
Proportional limit: The highest stress at which stress and strain are directly proportional. This is the point on the curve where the deviation from the straight-line portion begins.
Elastic limit: The greatest stress a material can withstand without any permanent strain.
Yield strength: The stress required to produce a small amount of plastic deformation.
Modulus of resilience: The work done on a unit volume of material as the force increases from zero to the elastic limit. It is also known as Young's modulus of elasticity, and is analogous to the stiffness of a spring.

## Slide 36
Hooke’s Law
For materials stressed in tension, at relatively low levels, stress and strain are proportional through:
Here, constant E is known as the modulus of elasticity, or Young’s modulus.
Within the linear region, a specific type of material will always follow the same curves despite different physical dimensions. Thus, it can say that the linearity and slope are a constant of the type of material only. In tensile and compressional stress, this constant is called the modulus of elasticity or Young's modulus (E). So,
where stress = F/A in N/m2 strain = Dl/l unit less
E = Modulus of elasticity in N/m2

## Slide 37
The modulus of elasticity has units of stress, that is, N/m2. The following table gives the modulus of elasticity for several materials. In an exactly similar fashion, the shear modulus is defined for shear stress-strain as modulus of elasticity.
Material | Modulus (N/m2)
Aluminum | 6.89 x 1010
Copper | 11.73 X 10'° 20.70 X 1010
Steel | 2.1 x 108

## Slide 38
Strain hardening refers to a material becoming stronger and harder with increasing strain, while strain softening means a material becomes weaker with increasing strain; essentially, in strain hardening, stress increases with deformation, whereas in strain softening, stress decreases with deformation as strain increases.

## Slide 39
Week 7
Pages 40-43
Basic Materials Properties

## Slide 40
Ductility:
Ductility describes the extent to which a material (or structure) can undergo large deformations before fracture. The term is used in earthquake engineering to designate how well a building will endure large lateral displacements imposed by ground shaking.
A ductile structure's ability to dissipate energy during an earthquake is, therefore, also advantageous as it will keep deforming without reaching ultimate failure or collapse. An example of a ductile structure is a properly detailed steel frame with that will enable it to undergo large deformations before the onset of failure.

## Slide 41
Figure: Brittle vs Ductile Material.

## Slide 42
Figure: What do you think which colour exhibits less ductile behaviour?????.

## Slide 43
True Stress versus Engineering Stress
While both "stress" and "strain" measure deformation in a material, the key difference between "true stress/strain" and "engineering stress/strain" lies in how the cross-sectional area is considered: "engineering" calculations use the original cross-sectional area of the material, while "true" calculations use the instantaneous, changing cross-sectional area during deformation, making true stress/strain values always higher than engineering stress/strain, especially at large deformations.

## Slide 44
Week 8
Pages 45-48
Basic Materials Properties

## Slide 45
Hardness
Hardness is the resistance of a material to localized plastic deformation. Hardness is a measure of a material's resistance to permanent deformation. Toughness is a measure of how much deformation a solid material can undergo before fracturing. Hardness is often inversely related to ductility, so the ductile metals mentioned above typically have relatively low hardness.
The product EI is termed the "beam stiffness", or sometimes the "flexural rigidity". It is often given the symbol Σ. It is a measure of how strongly the beam resists deflection under bending moments.

## Slide 46
Stiffness is how a component resists elastic deformation when a load is applied. Hardness is resistance to localized surface deformation.
The modulus of rigidity, also known as shear modulus, is defined as the ratio of shear stress to shear strain of a structural member. This property depends on the material of the member: the more elastic the member, the higher the modulus of rigidity.
Stiffness is the extent to which an object resists deformation in response to an applied force.
Elastic modulus is a measure of stiffness. Steel is stiffer than rubber thus its modulus is higher.
Stiff → not easily bent or changed in shape. Rigid → unable to bend or be forced out of shape, not flexible.
Rigidity, on the other hand, refers to the opposite property of elasticity. It is the inability of a material to deform under an external force. Flexibility is the ability of a material to bend, twist or stretch without breaking. This property depends on the material's elasticity and plasticity.

## Slide 47
Resilience
The resilience of the material is the triangular area underneath the elastic region of the curve. In physics and engineering, resilience is defined as the capacity of a material to absorb energy when it is deformed elastically and then, upon unloading to have this energy recovered.
Toughness
The area underneath the stress-strain curve is the toughness of the material- i.e. the energy the material can absorb prior to rupture.. It also can be defined as the resistance of a material to crack propagation. The ability of a metal to deform plastically and to absorb energy in the process before fracture is termed toughness. A material with high strength and high ductility will have more toughness than a material with low strength and high ductility.
Comparison between resilience and toughness of metals

## Slide 48
Poisson ratio
Poisson ratio is the ratio of transverse contraction (or expansion) strain to longitudinal extension strain in the direction of stretching force. Tensile deformation is considered positive and compressive deformation is considered negative.
Torque (Twisting Moment)
Torque typically refers to the tendency of a force to rotate an object around an axis. It is commonly used in the context of engines, vehicles, and rotating machinery. Torque is a measure of the rotational force applied to an object and is typically expressed in units such as newton-meters or foot-pounds.

## Slide 49
Week 9
Pages 50-51
Basic Materials Properties

## Slide 50
Hoop stress and longitudinal stress are two types of stress that occur in cylindrical pipes:
Hoop stress
Also known as tangential stress, this stress runs around the pipe in a ring-like pattern. It's caused by internal pressure and acts perpendicular to the pipe's axis and radius.
Longitudinal stress
This stress runs up the pipe in an axial direction. It occurs when the length of the pipe changes due to normal stress.
The relationship between hoop stress and longitudinal stress depends on the thickness of the pipe wall relative to its radius:
Thin-walled pipes
In most practical engineering applications, the hoop stress is about twice the magnitude of the longitudinal stress. This is because the wall thickness is small compared to the radius..
Longitudinal stress and Hoop stress

## Slide 51
Thick-walled pipes
In these cases, the relationship between the two types of stress is more complex and may require more advanced analysis.
Click this link
Hoop Stress
Longitudinal Stress

## Slide 52
Week 10
Pages 53-67
Shear Force and Bending moment diagram

## Slide 53: Moment and Bending moment
Moment: It is the product of force and perpendicular distance between line of action of the force and the point about which moment is required to be calculated.
Bending Moment (BM): The moment which causes the bending effect on the beam is called Bending Moment. It is generally denoted by ‘M’ or ‘BM’.

## Slide 54: SIGN CONVENTION FOR SHEAR FORCE
F
F
F
F
+ ve shear force
- ve shear force

## Slide 55: SIGN CONVENTION FOR BENDING MOMENTS
The bending moment is considered as Sagging Bending Moment if it tends to bend the beam to a curvature having convexity at the bottom as shown in the Fig. given below. Sagging Bending Moment is considered as positive bending moment.
Convexity
Fig. Sagging bending moment [Positive bending moment ]

## Slide 56: SIGN CONVENTION FOR BENDING MOMENTS
Similarly the bending moment is considered as hogging bending moment if it tends to bend the beam to a curvature having convexity at the top as shown in the Fig. given below. Hogging Bending Moment is considered as Negative
Bending Moment.
Fig. Hogging bending moment [Negative bending moment ]
Convexity

## Slide 57: SHEAR FORCE AND BENDING MOMENT DIAGRAMS (SFD & BMD)
Shear Force Diagram (SFD):
The diagram which shows the variation of shear force along the length of the beam is called Shear Force Diagram (SFD).
Bending Moment Diagram (BMD):
The diagram which shows the variation of bending moment along the length of the beam is called Bending Moment Diagram (BMD).

## Slide 58
Point of Contra flexure [Inflection point]:
It is the point on the bending moment diagram
where bending moment changes the sign from positive to negative or vice versa.
It is also called ‘Inflection point’. At the point of
inflection point or contra flexure the bending moment is zero.

## Slide 59: SFD & BMD Full Math

## Slide 60: Problem-1: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5 K
A
10′

## Slide 61: Solution:
10′
5 K
A
RA = 5 K
∑ Fy = 0
=> 5 - RA = 0
=> RA = 5 K.
MA = 50 K-ft.
∑ MA = 0
=> 5 x 10 - M𝐴 = 0
=> M𝐴 = 50 K-ft.
5 K
5 K
50 K-ft.
0 K-ft.
SFD
BMD

## Slide 62: Problem-2: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5 K
A
10′

## Slide 63: Solution:
A
RA = 5 K
∑ Fy = 0
A
=> 5 - R = 0
=> RA = 5 K.
MA = 50 K-ft.
∑ MA = 0
=> 5 x 10 - M𝐴 = 0
𝐴
=> M = 50 K-ft.
5 K
5 K
50 K-ft.
0 K-ft.
10′
5 K
SFD
BMD

## Slide 64: Problem-3: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
10′
5 K
A

## Slide 65: Solution:
RA = 5 K
∑ Fy = 0
=> - 5 + RA = 0
=> RA = 5 K.
MA = 50 K-ft.
∑ MA = 0
=> 5 x 10 - M𝐴 = 0
𝐴
=> M = 50 K-ft.
5 K
5 K
50 K-ft.
0 K-ft.
10′
5 K
A
SFD
BMD

## Slide 66: Problem-4: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5′
5 K
5′
A

## Slide 67: Solution:
RA = 5 K
∑ Fy = 0
=> 5 - RA = 0
=> RA = 5 K.
MA = 25 K-ft.
∑ MA = 0
=> - 5 x 5 + M𝐴 = 0
𝐴
=> M = 25 K-ft.
5 K
5 K
25 K-ft.
0 K-ft.
5′
5 K
5′
A
 | SFD |  | 
 | BMD |  | 

## Slide 68
Week 11
Pages 69-81
Shear Force and Bending moment diagram

## Slide 69: Problem-5: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5′
A
3 k/ft.
+ D
+ I
I
+ D
n = (n/n+1) * ab
n = (1/n+1) * ab
Small
a
b
Short Formula

## Slide 70: Solution:
RA = 15 K
A
∑ Fy = 0
=> 3 x 5 - R = 0
=> RA = 15 K.
MA = 50 K-ft.
2
2
=> 𝑤𝑙 - M = 0
𝐴
=> M𝐴 =
3 𝑥 52
2
= 37.5 K-ft.
0 K
15 K
∑ MA = 0
37.5 K-ft.
0 K-ft.
5′
A
3 k/ft.
10 Curve SFD
20 Curve BMD

## Slide 71: Solution:
5′
3 k/ft.
10′
5 K
10 Curve
5′
5 K
5′
SFD
BMD
 | SFD |  | 
 |  | 10 Curve | 
 | BMD |  | 
10 Curve SFD
20 Curve BMD

## Slide 72: Problem-6: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5′
A
3 k/ft.

## Slide 73: Solution:
RA = 15 K
MA = 37.5 K-ft.
15 K
0 K
0 K-ft.
5′
A
3 k/ft.
∑ Fy = 0
=> 3 x 5 - RA = 0
=> RA = 15 K.
∑ MA = 0
2
2
=> 𝑤𝑙 - M = 0
𝐴
=> M𝐴 =
3 𝑥 52
2
= 37.5 K-ft.
37.5 K-ft.
10 Curve
20 Curve
SFD
BMD

## Slide 74: Problem-7: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5′
A
3 k/ft.
5′

## Slide 75: Solution:
RA = 15 K
MA = 112.5 K-ft.
0 K
15 K
0 K-ft.
5′
A
3 k/ft.
5′
∑ Fy = 0
=> 3 x 5 - RA = 0
=> RA = 15 K.
∑ MA = 0
2
𝐴
=> wl (5 + 𝑙) - M = 0
𝐴
2
=> M =3 x 5 (5 + 5)= 112.5 K-ft.
10 Curve 15 |  | K | 
 | SFD |  | 
20 Curve 37.5 K |  | -ft. 10 Cu | 
 | BMD |  | 
112.5 K-ft.
rve

## Slide 76: Problem-8: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
9′
A
10 k/ft.

## Slide 77
Solution:
RA = 45 K
∑ Fy = 0
=> 0.5 x 9 x 10 - RA = 0
=> RA = 45 K.
MA = 135 K-ft.
∑ MA = 0
=> Area x cantorial distance - M𝐴 = 0
3
𝐴
=> 0.5 x 9 x 10 x 9 - M = 0
𝐴
=> M = 135 K-ft.
0 K
45 K
135 K-ft.
0 K-ft.
9′
A
10 k/ft.
x
2
9
V = - 1 . x . (10 . x)
9
2
= - 5 𝑥 [0≤x≤9]
x
9
3
M = - 5 𝑥 . 𝑥 [0≤x≤9]
2
w k/ft.
10 = 𝑤
9 𝑥
=> w =
10
9
. x
X
X
20 Curve SFD
30 Curve BMD

## Slide 78: Problem-9: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A 6′
10 k/ft.

## Slide 79
Solution:
RA = 30 K
MA = 120 K-ft.
0 K
30 K
120 K-ft.
0 K-ft.
rve
X
x
V = 30 - 1 . x . (10 . x)
= 30 -
2 6
5 𝑥2
6
5 𝑥2
6
.
𝑥 3
[0≤x≤6]
Mx = - 120 + 30x -
[0≤x≤6]
w k/ft.
6
=
10 𝑤
𝑥
6
=> w = 10 . x
X
6′
A
10 k/ft.
x | Vx (kip) | Mx (kip-ft.)
0 | 30 | - 120
2 | 26.67 | - 62.22
4 | 16.67 | - 17.78
6 | 0 | 0
20 Cu
SFD
30 Curve BMD

## Slide 80: Problem-10: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
6′
A
10 K
10 K
B
3′
3′

## Slide 81
Solution:
RA = 10 K
∑ Fy = 0
=> RA + RB - 10 - 10 = 0
=> RA = 20 - RB = 20 – 10 = 10 K
∑ MA = 0
=> 10 x 3 + 10 x (6 + 3) - R
B
x 12 = 0
=> RB x 12 = 30 + 90 = 120
B
=> R = 120/12 = 10 K
10 K
0 K-ft.
6′
A
10 K
10 K
B
3′
3′
RB = 10 K
10 K
0 K
30 K | SFD -ft. 30 | K-ft.
 | BMD | 

## Slide 82
Week 12
Pages 83-98
Shear Force and Bending moment diagram

## Slide 83: Problem-11: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
6′
A
10 K
4 K
B
3′
3′

## Slide 84
Solution:
RA = 8.5 K
∑ Fy = 0
=> RA + RB - 10 - 4 = 0
=> RA = 14 - RB = 14 – 5.5 = 8.5 K
∑ MA = 0
=> 10 x 3 + 4 x (6 + 3) - R
B
x 12 = 0
=> RB x 12 = 30 + 36 = 66
B
=> R = 66/12 = 5.5 K
5.5 K
25.5 K-ft.
0 K-ft.
6′
A
10 K
4 K
B
3′
3′
RB = 5.5 K
8.5 K
0 K
SFD
BMD
16.5 K-ft.
1.5 K

## Slide 85: Problem-12: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
4 K/ft.
10′
B

## Slide 86: Solution:
RA = 20 K
∑ MA = 0
=> (4 x 10) x 10 - R
B
x 10 = 0
2
=> RB x 10 = 200
=> RB = 200/10 = 20 K
∑ Fy = 0
=> RA + RB - 4 x 10= 0
=> RA = 40 - RB = 40 – 20 = 20 K
20 K
0 K-ft.
RB = 20 K
20 K
0 K
10′
A
4 K/ft.
B
 | SFD |  | 
0.5 x 20 x 5 |  | = 50 K-ft. | 
 | BMD |  | 

## Slide 87: Problem-13: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
6′
A
6 K
B
3′
3′
3 K/ft.

## Slide 88: Solution:
RA = 15 K
∑ MA = 0
=> (3 x 6) x 3 + 6 x (6 + 3) - RB x 12 = 0
=> RB x 12 = 54 + 54 =108
=> RB = 108/12 = 9 K
∑ Fy = 0
=> RA + RB - 3 x 6 - 6 = 0
=> RA = 24 - RB = 24 – 9 = 15 K
0 K
9 K
0 K-ft.
RB = 9 K
15 K
SFD
BMD
3 K
6′
A
6 K
B
3′
3′
3 K/ft.
15 x
6
(15+3)
= 5′
5′
1′

## Slide 89: Problem-14: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
10′
A
5 K
C
5′
3 K/ft.
B

## Slide 90: Solution:
RA = 12.5 K
∑ MA = 0
=> (3 x 10) x 5 + 5 x (10 + 5) - RB x 10 = 0
=> RB x 10 = 150 + 75 = 225
=> RB = 225/10 = 22.5 K
∑ Fy = 0
=> RA + RB - 3 x 10 - 5 = 0
=> RA = 35 - RB = 35 – 22.5 = 12.5 K
5 K
26.06 K-ft.
0 K-ft.
RB = 22.5 K
12.5 K
0 K
SFD
BMD
17.5 K
4.167′
5.833′
25 K-ft.
10′
A
5 K
C
5′
3 K/ft.
B

## Slide 91: Problem-15: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
2′
A
12 K
E
2′
2 K/ft.
B
6 K
2′
2′
C
D

## Slide 92
Solution:
y
∑ F = 0
=> RB + RE - 2 x 2 - 6 - 12 = 0
=> RB = 22 - RE = 22 – 9.33 = 12.67 K
E
x 6 = 0
∑ MB = 0
=> - (2 x 2) x 1 + 6 x 2 + 12 x 4 - R
=> RE x 6 = 34
=> RE = 34/6 = 9.33 K
0 K
0 K
4 K-ft.
0 K-ft.
RE = 9.33 K
SFD
BMD
4 K
2′
A
12 K
E
2′
2 K/ft.
B
6 K
2′
2′
C
D
RB = 12.67 K
8.67 K
2.67 K
9.33 K
0 K-ft.

## Slide 93: Problem-16: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
6′
A
C
3 K/ft.
B
10′
2 K/ft.

## Slide 94: Solution:
RB = 20.8 K
∑ MB = 0
3
=> - (0.5 x 6 x 3) x (1 x 6) + 2 x 10 x 5 -
RC x 10 = 0
=> RC x 10 = 82
=> RC = 82/10 = 8.2 K
∑ Fy = 0
=> RB + RC - 0.5 x 6 x 3 – 2 x 10= 0
=> RB = 29 - RC = 29 – 8.2 = 20.8 K
0 K
0 K
18 K-ft.
0 K-ft.
RC = 8.2 K
9 K
16.81 K-ft.
11.8 K
8.2 K
0 K-ft.
6′
A
C
3 K/ft.
B
10′
2 K/ft.
5.9′
4.1′
SFD
BMD

## Slide 95: Problem-17: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
3 K/ft.
12 K
6 K
E
D
2′ B
2′
2′
3′

## Slide 96
Solution:
0 K
0 K
13 K-ft.
0 K-ft.
RD = 16 K
0 K-ft.
A
C
3 K/ft.
6 K 12 K
E
D
2′ B
2′
2′
3′
14 K-ft.
9 K-ft.
RA = 6.5 K
6.5 K
0.5 K
4.5 K
11.5 K
SFD
BMD
∑ MA = 0
3
=> 6 x 2 + 12 x 4 – 0.5 x 3 x 3 x (6 + 2 x
3) - RD x 6 = 0
=> RD = 16 K

## Slide 97: Problem-18: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
2 K/ft.
B
10 K
10 K-ft.
D
2′
2′
4′

## Slide 98
Solution:
RB = 1.5 K
0 K
0 K-ft.
RC = 16.5 K
0 K-ft.
1.5 K
6.5 K
10 K
0 K
SFD
BMD
A
C
2 K/ft.
B
10 K
10 K-ft.
D
2′
2′
4′
∑ MB = 0
=> - 10 + 2 x 4 x 2 + 10 x 6 - RC x 4 = 0
=> RC = 66/4 = 16.5 K
9.11 K-ft.
20 K-ft.
10 K-ft.
0.75′
3.25′

## Slide 99
Week 13
Pages 100-127
Shear Force and Bending moment diagram

## Slide 100: Problem-19: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
3 K/ft.
B
6 K
D
2′
1′
3′
1′
2 K/ft.

## Slide 101
Solution:
B
R = 4.5 K
0 K
0 K
0 K-ft.
RC = 10 K
0 K-ft.
4 K
5.5 K
4.5 K
SFD
BMD
4 K-ft.
9 K-ft.
A
C
3 K/ft.
B
6 K
D
2′
1′
3′
1′
2 K/ft.
0.5 K
3.5 K-ft.
∑ MB = 0
=> - 2 x 2 x 1 + 6 x 1 + 0.5 x 3 x 3 x (2 +
3
2 x 3) - R
C
x 2 = 0
=> RC = 20/2 = 10 K

## Slide 102: Problem-20: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
3 K/ft.
B
C D
3′
3′
4′ 2′
E
6 K
2 K/ft. 10 K-ft.

## Slide 103
Solution:
B
R = 6.25 K
0 K
0 K
0 K-ft.
D
R = 8.25 K
2.5 K-ft.
4.5 K
1.75 K
SFD
BMD
4.5 K-ft.
10 K-ft.
A
3 K/ft.
B
C D
3′
3′
4′ 2′
E
6 K
2 K/ft. 10 K-ft.
4.25 K
8.25 K
0 K-ft.
B
∑ M = 0
3
=> - 0.5 x 3 x 3 x 1 x 3 + 6 x 4 + 2 x 2 x 5
+ 10 - RD x 6 = 0
=> RD = 49.5/6 = 8.25 K

## Slide 104: Problem-21: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
3 K/ft.
B
10 K
3′
3′
2 K/ft.
E
4
3
C D
2′ 2′ 2′
F

## Slide 105
Solution:
RB = 9.25 K
0 K
0 K
0 K-ft.
RE = 11.75 K
0.25 K
1.75 K
SFD
BMD
8 K
9 K
0 K-ft.
3
x 10 = 6 K
A
3 K/ft.
42+32
10 K
3′
C
2′
3′
2 K/ft.
4
3
D
2′ 2′
F
4
42+32
x 10 = 8 K
A
3 K/ft.
B
D
3′
3′
2 K/ft.
E
C
2′ 2′ 2′
F
8 K
3.75 K
0.125′
1.875′
6 K
B E
∑ MB = 0
=> - 3 x 3 x 1.5 + 2 x 2 x 3 + 8 x 9 - RE x
6 = 0
=> RE = 11.75 K

## Slide 106: Problem-22: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
B
D
3′ 4′
5′
5 K
4 K/ft.
C
E
4′
F
8 K

## Slide 107: => - 15 + 4 x4 x 2 + 8 x 13 - RD x 8 = 0
Solution:
RB = 8.875 K
0 K
0 K
0 K-ft.
RD = 15.125 K
SFD
BMD
8.875 K
0 K-ft.
A
5 K
F
15 K-ft.
5 K
F
15 K-ft.
A
5 K
0 K
5 K
0 K
5 K
3′
0 K-ft.
0 K-ft.
15 K-ft.
7.125 K
A
B
D
3′
4′
5′
4 K/ft.
C
E
4′
15 K-ft.
8 K
A
B
5 K
D
3′ 4′
5
′
5 K
4 K/ft.
C
E
4′
F
3′
8 K
A
B
D
3′
4′
5′
4 K/ft.
C
E
4′
15 K-ft.
8 K
8 K
2.22′
1.78′
40 K-ft.
11.5 K-ft.
∑ MB = 0
=> RD = 15.125 K
SFD
BMD

## Slide 108: Problem-23: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
3′
6′
E
8 K
10 K
3′ 2′
Link
4 K/ft.

## Slide 109: => 8 x 3 + 10 x 6 - RD x 8 = 0
Solution:
RB = 7.5 K
0 K
0 K
0 K-ft.
RD = 10.5 K
SFD
BMD
7.5 K
0 K-ft.
0.5 K
10.5 K
C
D
3′
E
8 K
B
10 K 4 K/ft.
3′ 2′ 6′
A
C
B
3′
8 K
10 K
D
3′ 2′ A
6′
4 K/ft.
E
RD = 10.5 K
RE = 34.5 K
SFD
BMD
34.5 K
0 K
10.5 K
0 K
0 K-ft.
0 K-ft.
135 K-ft.
∑ MA = 0
=> RD = 10.5 K
135 K-ft.

## Slide 110: Problem-24: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
5 m
15 kN/m.
E
10 kN-m.
1 m
1 m
3 m

## Slide 111
Solution:
0 K
0 K
0 K-ft.
RD = 23.33 K
8.1 K-ft.
1.75 K
SFD
BMD
10 K-ft.
RB = 36.67 K
21.67 K
0 K-ft.
A
C
B
D
5 m
15 kN/m.
E
10 kN-m.
1 m
1 m
3 m
1.44 m
23.33 K
1.56 m
∑ MC = 0
=> - 15 x 4 x 2 + 10 - RB x 3 = 0
=> RB = 36.67 K

## Slide 112: Problem-25: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
50 K/ft.
E
500 K
6′
8′
6 D
8′
7′
300 K
F

## Slide 113
Solution:
RA = 440 K
0 K
0 K
0 K-ft.
RF = 160 K
160 K
1120 K-ft.
40 K
0 K-ft.
A
∑ M = 0
=> 50 x 8 x 10 + 500 x 20 – 300 x 28 -
RF x 36 = 0
=> RF = 160 K
A
C
B
50 K/ft.
E
500 K
6′
8′
6 D
8′
7′
300 K
F
440 K
460 K
SFD
BMD

## Slide 114: Problem-26: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
10 K/ft.
8′
8′
6′
12′
12 K/ft.
Link

## Slide 115: => - 40 x 8 + 0.5 x 6 x12 x 2 x 6 + 0.5 x 12 x 12 x (6 + 1 x 12) - R
Solution:
0 K-ft.
0 K
30.22 K
320 K-ft.
3
30.22 x 12 – 0.5 x 12 x 12 x 1 x 12 = 74.64 K-ft.
0 K
40 K
0 K-ft.
440 K
77.78 K
SFD
BMD
A
C
B
D
10 K/ft.
8′ 8′
6′
12′
12 K/ft.
RB = 40 K
RD = 30.22 K
C
B
D
8′
6′
12′
RC = 117.78 K
12 K/ft.
C
∑ M = 0
3 3
D
x 18 = 0
D
=> R = 30.22 K
41.78 K
A
10 K/ft.
8′
B
RB = 40 K
RA = 40 K
SFD
40 K
0 K
0 K-ft.
0 K-ft.
80 K-ft.
0 K
40 K
BMD

## Slide 116: Problem-27: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
4′
A
40 K
C
2′
20 K/ft.
B
1′
D

## Slide 117
Solution:
RA = 32 K
C
x 5 = 0
∑ MA = 0
=> (20 x 4) x 2 + 40 x 7 - R
=> RC = 88 K
40 K
RC = 88 K
32 K
0 K
SFD
BMD
4′
A
40 K
C
2′
20 K/ft.
B
1′
D
1.6′
48 K
2.4′
25.6 K-ft.
0 K-ft.
32 K-ft.
80 K-ft.

## Slide 118: Problem-28: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
4′
A
5 K
C
2′
10 K/ft.
B
3′
D
8 K
3′

## Slide 119
Solution:
∑ MA = 0
=> 10 x 4 x 2 + 8 x 7 + 5 x 12 - R
C
x 10 = 0
C
=> R = 19.6 K
5 K
0 K-ft.
RC = 19.6 K
SFD
BMD
6.6 K
10 K-ft.
3.34′
RA = 33.4 K
33.4 K 0.66′
0 K
33.8 K-ft.
4′
A
5 K
C
2′
10 K/ft.
B
3′
D
8 K
3′
14.6 K
53.3 K-ft.

## Slide 120: Problem-29: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
4′
2 K/ft.
B
4′
D
4′ 4′
E
50 K
150 K-ft.

## Slide 121
Solution:
RA = 45.83 K
D
x 12 = 0
∑ MA = 0
=> 50 x 4 – 150 + 2 x 8 x 12 - R
=> RD = 20.17 K
8 K
RD = 20.17 K
45.83 K
BMD
0 K
4.17 K
4′
A
50 K
C
4′
2 K/ft.
B
4′
D
4′
E
150 K-ft.
12.17 K
SFD
183.32 K-ft.
0 K-ft.
16 K-ft.

## Slide 122: Problem-30: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
10 K
C
B
10′
D
15′

## Slide 123
A
10 K
Solution:
C
B
10′
D
15′
∑ Fx = 0
=>𝐻𝐴 = 𝐻𝐷 = 10/2 = 5 K
∑ MA = 0
=> 10 x 10 –RD x 15 = 0
=> RD = 6.67 K
A
10 K
C
B
D
5 K
6.67 K
5 K
6.67 K
25 K-ft.
5 K
A
6.67 K
5 K B
6.67 K
5 K
0 K
0 K-ft.
0 K-ft.
0 K
25 K-ft.
0 K
6.67 K
0 K
SFD
BMD
AFD
25 K-ft.
D
C
5 K
6.67 K
5 K
6.67 K
5 K
0 K
0 K-ft.
0 K-ft.
0 K
25 K-ft.
6.67 K
0 K
0 K
SFD
BMD
AFD
15
′
C
6.67 K
SFD
BMD
10 K
0 K
6.67 K
25 K-ft.
25 K-ft.
6.67 K
0 K
6.67 K
25 K-ft.
0 K-ft.
AFD
B
5 K
5 K
10 K
0 K
0 K-ft.
25 K-ft.
10 K
0 K
(-)
(+)
(-)

## Slide 124: Problem-31: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
10 K
C
B
10′
D
15′
E
F

## Slide 125
Solution:
∑ Fx = 0
=>𝐻𝐴 = 𝐻𝐷 = 10/2 = 5 K Assume, 𝐵𝑀𝐸 = 𝐵𝑀𝐹 = 0
∑ ME = 0 [Considering AE part only]
=> 5 x 5 –MA = 0 => MA = 25 K
15′
C
3.33 K
SFD
BMD
10 K
25 K-ft.
B
25 K-ft.
3.33 K
0 K
3.33 K
25 K-ft.
0 K-ft.
AFD
5 K
5 K
A
10 K
C
B
10′
15′
E
F
D
10 K
A
5 K
3.33 K
B
E
25 K-ft.
C F
25 K-ft.
5 K D
3.33 K
∑ MA = 0
=> - 25 - 25 + 10 x 10 - 𝑉𝐷 x 15 = 0
=> VD = 3.33 K; VA = - 3.33 K
10 K
0 K
10 K
0 K
25 K-ft.
A
5 K
3.33 K
5 K B
3.33 K
5 K
0 K
0 K
25 K-ft.
0 K-ft.
0 K
3.33 K
0 K
SFD
BMD
AFD
25 K-ft.
0 K-ft.
25 K-ft.
(+)
(-)
25 K-ft.
0 K-ft.
25 K-ft.
A
B
5 K
3.33 K
0 K
3.33 K 5 K
3.33 K
5 K
0 K
0 K
25 K-ft.
0 K-ft.
3.33 K
0 K
0 K
SFD
BMD
AFD
25 K-ft.
0 K-ft.
25 K-ft.
(-)

## Slide 126: Problem-32: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
4′
4′
2 K/ft.
4′
8 K-ft.
Link

## Slide 127: ∑ MB = 0 => 8 - RD x 8 = 0 => RD = 1 K
Solution:
RB = 1 K
0 K-ft.
RD = 1 K
SFD
BMD
4 K-ft.
0 K
1 K
0 K-ft.
0 K
1 K
B
C
D
4′
4′
4 K-ft.
4′
2 K/ft.
B
RD = 10.5 K
RB = 1 K
7 K
0 K
0 K-ft.
A
C
B
D
4
′
4
′
2 K/ft.
4
′
8 K-ft.
8 K-ft.
RA = 7 K
A
12 K-ft.
0 K
1 K
0 K-ft.
12 K-ft.
K-ft.
 |  | 0.5′
3.5′ SFD |  | 0.25
 | BMD | 

## Slide 128
Week 14
Pages 129-174
Shear Force and Bending moment diagram

## Slide 129: Problem-33: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
D
2′
2′
400 lb/ft.
B
1′ C
200 lb/ft.
600 lb
4′
E

## Slide 130
Solution:
RB = 1680 lb
∑ MB = 0
=> - 400 x 2 x 1 + 600 x 1 +
200 x 6 x 4 - RD x 5 = 0
=> RD = 920 lb
0 lb
800 lb-ft.
0 lb-ft.
RD = 920 lb
520 lb
800 lb
SFD
BMD
400 lb-ft.
A
B
D
2′
2′
400 lb/ft.
200 lb/ft.
600 lb
1′ C 4′
E
880 lb
400 lb
1.4′
0.5′ 0 lb
2.6′
276 lb-ft.
80 lb-ft.
0 lb-ft.

## Slide 131: Problem-34: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
B
D
C
2′
4′
2 lb/ft.
4′
40 lb
8 lb

## Slide 132
Solution:
RA = 26 lb
∑ MB = 0
=> 2 x 8 x 4 + 40 x 4 + 8 x 10 -
RC x 8 = 0
=> RC = 38 lb
0 lb
0 lb-ft.
RC = 38 lb
22 lb
30 lb
SFD
16 lb-ft.
BMD
0 lb
26 lb
8 lb
80 lb-ft.
88 lb-ft.
0 lb-ft.
A
C
B
D
2′
4′
2 lb/ft.
4′
40 lb
8 lb
18 lb

## Slide 133: Problem-35: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
6′
6′
2 lb/ft.
5′
D

## Slide 134
Solution:
B
D
36 lb-ft.
12 lb
A
C
B
36 lb-ft.
D
6′
6′
2 lb/ft.
RD = 12 lb
5′
36 lb-ft. 5′
12 lb
0 K
0 K
36 lb-ft.
0 lb-ft.
12 K
0 K
0 K
SFD
BMD
AFD
36 lb-ft.
0 lb-ft..
(-)
A
C
B
6′
6′
∑ MD = 0
=> - 2 x 6 x 3 + MD = 0
=>MD= 36 lb-ft.
2 lb/ft.
12 lb
36 lb-ft.
12 lb
BMD
SFD
36 lb-ft.
0 lb
0 lb-ft.
0 lb
0 lb-ft.

## Slide 135: Problem-36: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
2.5′
5′
1 lb/ft.
10 lb
E
5′
B C D
2.5′
1 lb/ft.

## Slide 136
Solution:
RA = 10 lb
∑ M = 0
B
=> 1 x 5 x 2.5 + 10 x 7.5 + 1 x
5 x 12.5 - RE x 15 = 0
=> RE = 10 lb
0 lb
0 lb-ft.
RE = 10 lb
5 lb
10 lb
BMD
SFD
50 lb-ft.
0 lb
37.5 lb-ft.
0 lb-ft.
10 lb
5 lb
A
2.5′
5′
1 lb/ft.
10 lb
E
5′
B C D
2.5′
1 lb/ft.
37.5 lb-ft.

## Slide 137: Problem-37: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
2′
3′ 3′
3′
10 lb
E
Link
20 lb-ft.

## Slide 138: => 10 x 2 - RC x 5 = 0
Solution:
RA = 6 lb
0 lb
0 lb
0 lb-ft.
RC = 4 lb
SFD
BMD
12 lb-ft.
6 lb
0 lb-ft.
4 lb
A
C
B
3′
2′
10 lb
E
RC = 4 K
SFD
BMD
0 lb
4 lb
0 lb-ft.
0 lb-ft.
44 lb-ft.
∑ MA = 0
=> RC = 4 lb
44 K-ft.
A
C
D
3′
2′ B
3′
20 lb-ft.
3′
10 lb
E
C
3′
RE = 4 lb
3′
20 lb-ft.
D
0 lb
4 lb
12 lb-ft.
32 lb-ft.

## Slide 139: Problem-38: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
8′
8′
6′
12′
12 k/ft.
100 k

## Slide 140: Solution:
0 K
0 K-ft.
0 K
3.55 K
800 K-ft.
3
- 3.55 x 12 + 0.5 x 12 x 12 x 1 x
12 = 245.4 K-ft.
100 K
0 K-ft.
104.45 K
SFD
BMD
100 k
RD = 3.55 K
C
B
D
8′
6′
12′
RC = 204.45 K
12 K/ft.
∑ MC = 0
2
3
=> - 100 x 8 + 0.5 x 6 x12 x x 6 + 0.5 x
12 x 12 x (6 + 1 x 12) - R
D
x 18 = 0
3
=> RD = 3.55 K
68.45 K
8′
A

## Slide 141: Problem-39: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
D
6′
B 2′
4′
9 k
6 k/ft.
Link
8 k/ft.

## Slide 142
Solution:
0 K
0 K-ft.
2.17 K
34.17 K
0 K-ft.
24.83 K
0 K
SFD
BMD
RD = 34.17 K
RA = 24.83 K
∑ MC = 0
3
=> 0.5 x 6 x 6 x 1 x 6 + 9 x 6 + 8 x 4 x 10 -
RD x 12 = 0
=> RD = 34.17 K
6.83 K
76.98 K-ft.
72.64 K-ft.
A
C
D
6′
B 2′
4′
8 k/ft.
9 k
6 k/ft.

## Slide 143: Problem-40: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
B
C
10′
10′
3 k
2 k

## Slide 144
Solution: | 70 K-ft. | A | 10′ | 3 k B | 10′ | 2 k C | ∑ MA = 0 => MA = 3 x 10 + 2 x 20 = 70 k-ft. ∑ Fy = 0
 |  | RA = 5 K |  |  |  |  | => RA = 3 K + 2 K = 5 K
5 K 2 K 0 K 0 K SFD 0 K-ft. 0 K-ft. 20 K-ft. 70 K-ft. BMD |  |  |  |  |  |  | 

## Slide 145: Problem-41: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
B
C
6′
6′
6 k/ft.

## Slide 146: Solution:
0 K
0 K-ft.
3 K
0 K-ft.
15 K
0 K
SFD
BMD
C
R = 3 K
A
R = 15 K
∑ MA = 0
=> 0.5 x 6 x 6 x
1
3
x 6 - RC x 12 = 0
C
=> R = 3 K
A
B
C
6′
6′
3 x 8.45 + 0.
1
5 x 2.45 x 2.45 x x 2.45
3
= 22.89 K-ft.
x
2
V = 15 - 1 . [6 + (6-x)] . x
2
=> 0 = 15 - 12 𝑥 − 𝑥
2
=> x = 3.55′
w k/ft.
6 k/ft.
6 = 𝑤
6 (6−𝑥)
=> w = (6 - x)
X
3.55′
2.45′
6 - X
18 K-ft.

## Slide 147: Problem-42: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
6′
6′
2 lb/ft.

## Slide 148
Solution:
∑ MD = 0
=> - 2 x 6 x 3 + 2 x 6 x 3 + MD = 0
=>MD= 0 lb-ft.
B
D
24 lb
A
C
B
0 lb-ft.
D
6′
6′
2 lb/ft.
RD = 24 lb
5′
5′
0 lb-ft.
0 lb-ft.
24 lb
0 K
0 K
0 lb-ft..
0 lb-ft.
24 K
0 K
0 K
SFD
BMD
AFD
(-)
A
C
6′
6′
2 lb/ft.
B
24 lb
0 lb-ft.
12 lb
BMD
SFD
36 lb-ft.
0 lb
0 lb-ft.
0 lb
0 lb-ft.
12 lb

## Slide 149: Problem-43: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
5′
A
10 K
10 K
B
5′
5′
2 k/ft.

## Slide 150
Solution:
RA = 15 K
∑ MA = 0
=> 10 x 5 + 2 x 5 x 7.5 + 10 x 10 -
RB x 15 = 0
=> RB = 15 K
15 K
30 K-ft.
0 K-ft.
RB = 15 K
15 K
0 K
SFD
BMD
30 K-ft.
5′
A
10 K
10 K
B
5′
5′
2 k/ft.
48.75 K-ft.

## Slide 151: Problem-44: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
6′
A
6 K
C
5′
5 K/ft.
B
5′
6 K-ft.

## Slide 152
Solution:
RA = 3.5 K
∑ MA = 0
=> 6 + 6 x 6 + 5 x 5 x 13.5 - R
B
x 11 = 0
B
=> R = 34.5 K
0 K
25 K
0 K-ft.
RB = 34.5 K
SFD
BMD
3.5 K
9.5 K
62.5 K-ft.
6′
A
6 K
C
5′
5 K/ft.
B
5′
6 K-ft.
0 K
15 K-ft.
21 K-ft.

## Slide 153: Problem-45: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
5′
A
C
5′
B
1′
10 K
2′

## Slide 154
Solution:
0 K
0 K
0 K-ft.
7 K
15 K-ft.
0 K-ft.
3 K
SFD
BMD
RA = 3 K
∑ MB = 0
=> MB = 10 x 2 = 20 k-ft. [Clockwise]
∑ M = 0
A
=> 20 + 10 x 5 - RC x 10 = 0
=> RC = 7 K
35 K-ft.
5′
A
10 K
C
5′
B
1′
2′
20 K-ft.
5′
A
10 K
C
5′
B
RC = 7 K

## Slide 155: Problem-46: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
C
100 K
1
1
A
B
D
15′
6′
6′
Link

## Slide 156
Solution:
RA = 28.28 K
0 K
0 K
0 K-ft.
RC = 99 K
50 2 K
0 K-ft.
.
∑ MA = 0
=> 50 2 x 21 - RC x 15 = 0
=> RC = 99 K
50 2 K
C
A
B
15′
6′
1
x 100 = 50 2 K
12+12
C
12+12
100 K
1 x 100 = 50 2 K 1
1
A
D
15′ B
6′ 6′
28.28 K |  |  | 
 | SFD |  | 
 |  | 424.26 K-ft | 
 | BMD |  | 
SFD | 
BMD | 
0 K
0 K
0 K-ft.
0 K-ft.
0 K
D
C

## Slide 157: Problem-47: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
C
B
8′
10′
A
10 K

## Slide 158
Solution:
∑ MA = 0
=>MA= 10 x 8 lb-ft. = 80 lb-ft.
B
A
80 lb-ft.
10 lb
80 lb-ft. 10′
10 lb
0 K
0 K
0 lb-ft.
10 K
0 K
0 K
SFD
BMD
AFD
(-)
C
8′
80 lb-ft.
12 lb
BMD
SFD
80 lb-ft.
0 lb
0 lb-ft.
0 lb
0 lb-ft.
10 lb
80 lb-ft.
A
C
B
8′
RA = 10 lb
10′
10 K
10 K
B
10 lb
0 lb-ft..
80 lb-ft.

## Slide 159: Problem-48: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
A
6 K/ft.
B
6 K
4′
C 2′ D 2′
5′
2 K/ft.
E

## Slide 160
Solution:
B
R = 22.33 K
0 K
0 K-ft.
E
R = 5.67 K
10.65 K-ft.
12 K
10.33 K
SFD
11.34 K-ft.
16 K-ft.
BMD
0.33 K
0 K-ft.
∑ MB = 0
3
=> - 0.5 x 4 x 6 x 1 x 4 + 2 x 5 x 2.5 + 6 x
7 - RE x 9 = 0
=> RE = 5.67 K
A
C
6 K/ft.
B
6 K
4′
2′ D 2′
5′
2 K/ft.
E
0 K
5.67 K

## Slide 161: Problem-49: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
2.5′
A
C
2′
10 K/ft.
B
1.5′
50 K
200 K-ft.
1′
25 K

## Slide 162
Solution:
A
R = 21.25 K
0 K
0 K-ft.
RB = 121.25 K
0 K
21.25 K
46.25 K
0 K-ft.
84.375 K-ft.
∑ MA = 0
=> 10 x 2.5 x 1.25 + 200 + 50 x 4 +
25 x 7 - RB x 5 = 0
=> RB = 120 K
SFD
BMD
2.5′
A
C
2′
10 K/ft.
B
1.5′
50 K
200 K-ft.
1′
25 K
96.25 K
25 K
153.75 K-ft.
46.25 K-ft.
50 K-ft.

## Slide 163: Problem-50: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
10′
A
10 K
C
B
5′
4 K
10′
10′
5′
10′
20′
D
E
F

## Slide 164
Solution:
RE = 2.5 K
0 K
0 K
0 K-ft.
RF = 0.5 K
2 K
0 K-ft.
SFD
BMD
0.5 K
D
F
E
5′
20′
2 K
10 K-ft.
RA = 4.5 K
0 K
0 K
0 K-ft.
RB = 7.5 K
4.5 K
0 K-ft.
SFD
BMD
5.5 K
A
10 K
C
5′
B
10′
2 K
10′
2 K
45 K-ft.
10 K-ft.
10 K-ft.
BMD
0 K-ft.
0 K-ft.
RC = 2 K RD = 2 K
0 K
2 K
SFD
C D
5′ 5′
10′
A
10 K
C
B
5′
4 K
10′
10′
5′
10′
20′
4 K
D
E
F
2 K
0 K

## Slide 165: Problem-51: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam ABC.
25′
A
10 K
C
B
25′
25′
25′
25′
25′
D
E
F
25′
10 K
2 K/ft.

## Slide 166
Solution:
0 K-ft.
A
10 K
C
B
25′
25′
25′
25′
25′
D
E
F
25′
10 K
2 K/ft.
RE = 36.25 K
0 K
0 K
RF = 1.25 K
25 K
SFD
BMD
11.25 K
D
F
E
5′
10′
25 K
10′
10 K
1.25 K
12.5 K-ft.
125 K-ft.
RA = 1.25 K
0 K
0 K-ft.
RB = 36.25 K
1.25 K
SFD
BMD
11.25 K
A
25′
10 K
C
5′
B
10′
25 K
10′
25 K
12.5 K-ft.
0 K-ft.
0 K
0 K-ft.
312.5 K-ft.
0 K
0 K-ft.
0 K-ft.
C
D
RC = 25 K
RD = 25 K
25 K
25′
2 K/ft.
25 K
0 K
BMD
SFD

## Slide 167: Problem-52: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
D
5′
3′
4 K/ft.
5′
15 K-ft.

## Slide 168: Solution:
RB = 12.3 K
0 K
0 K
0 K-ft.
RD = 0.3 K
SFD
BMD
16.5 K-ft
0.3 K
0 K-ft.
12 K
18 K-ft.
A
C
B
D
5′
3′
4 K/ft.
5′
15 K-ft.
∑ MB = 0
=> - 4 x 3 x 1.5 + 15 - RD x 10 = 0
=> RD = - 0.3 K
1.5 K-ft.
.

## Slide 169: Problem-53: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
B
2′
4′
2 K
1 K/ft.

## Slide 170: Solution:
RA = 3.67 K
0 K
0 K-ft.
RB = 4.33 K
SFD
BMD
6.68 K-ft.
0 K
4.33 K
0 K-ft.
3.67 K
6.73 K-ft.
∑ MA = 0
=> 1 x 6 x 3 + 2 x 4 - RB x 6 = 0
=> R𝐵 = 4.33 K
A
B
2′
4′
1 K/ft.
2 K
1.4 K
2.33 K
0.33 K
3.67′
0.33′

## Slide 171: Problem-54: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
C
B
2 K/ft.
8′
6′
3 K/ft.
Link
50 K
10 K
4′
4′ D 2′
2′
E

## Slide 172: ∑ M = 0 => - 0.5 x 6 x 3 x 1 x 6 + 50 x 8 + 2 x 4 x 14 + 5 x 16 - R
Solution:
0 K
0 K-ft.
18 K-ft.
9 K
0 K-ft.
15.17 K
SFD
BMD
RC = 47.83 K
RB = 24.17 K
B
3
C
x 12 = 0
C
=> R = 47.83 K
34.83 K
A
B
E
R = 5 K
D
R = 5 K
5 K
0 K
0 K-ft.
0 K-ft.
SFD
10 K-ft.
0 K
5 K
BMD
A
B
8
′
6
′
3 K/ft.
50 K
10 K
2
′
E
2 K/ft.
C
4′ 4′ D 2′
10 K
2′ 2′
A
C
B
D
8′
6′
3 K/ft.
4′
4′
50 K 2 K/ft. R
D
= 5 K
103.36 K-ft.
35.96 K-ft.
13 K
5 K
0 K

## Slide 173: Problem-55: Find the SFD (Shear Force Diagram) & BMD (Bending Moment Diagram) of the following beam.
A
B
5′
20′
D
C
5′
10 K 10 K
2 K/ft.

## Slide 174: ∑ MA = 0 => -10 x 10 – 10 x 5 + 2 x 20 x 10 - RD x 20 = 0
Solution:
RC = 47.5 K
0 K-ft.
RD = 12.5 K
SFD
BMD
50 K-ft.
0 K
10 K
20 K
27.5 K
39.0625 K-ft.
0 K-ft.
=> RD = 10.5 K
A
B
5′
20′
2 K/ft.
D
C
5′
10 K 10 K
0 K
12.5 K
13.75′
6.25′
150 K-ft.

## Slide 175
Week 15
Pages 176-181
Beam Deflection

## Slide 182
Week 16
Pages 183-204
Beam Deflection Methods
(Double Integration and
Area Moment)

## Slide 201
Important Figures

## Slide 202
Important Figures

## Slide 203
Important Links
Beam Deflection 1
Beam Deflection 3
Beam Deflection 2
Beam Deflection 4
Beam Deflection 5

## Slide 204
Flexural Rigidity (EI)
Flexural Strength Flexural strength is a measure of a beam's ability to withstand bending and resist failure. It's a measure of a beam's tensile strength, and is determined by the highest stress the material can withstand before it fails. Flexural Rigidity (EI)
In plain simple words, without mathematical formula, for the benefit of non-civil engineers, it is a measure of the resistance to bending. The more difficult it is to bend it, the higher the flexural stiffness.
A plastic scale bends easily. It has very poor flexural stiffness.
The solid pen is not so easy to bend. Its “flexural stiffness” is high.
The relationship between stiffness and ductility is sort of opposite kind. A stiff material cannot be bent or, elongated at ease. But a ductile material can be bent, elongated, hammered without causing any fracture. A stiff material cannot permanently deform like a ductile material.
Hardness (KN/m2) and stiffness (KN/m) are both properties of materials that measure how they resist deformation, but they measure different types of deformation and have different units of measurement.

## Slide 205
Week 17

## Slide 206
Any Questions?

## Slide 207
Thank you for your kind attention
Courtesy/Acknowledgement
Massachusetts Institute of Technology
Texas Tech University
Rajshahi University of Engineering & Technology
Mumbai Institute of Technology
Dhaka International University
Daffodil International University
Special Thanks: Faruque Abdullah (RUET/DIU)